## Slide 1: Mastering Wi-Fi PCAP Analysis Packet Capture & Analysis Techniques
Rasika Nayanajith (@mrncciew)
Every Wi‑Fi problem leaves a trace
Notes: Packet captures are incredibly powerful for Wi‑Fi troubleshooting. But capturing is only half the battle—and analyzing frame by frame simply doesn’t scale.
Today, I’ll show you different ways to capture and analyze Wi‑Fi traffic, so you can quickly find issues without getting lost in the noise.”

## Slide 2
Rasika Nayanajith (@mrncciew)
Wireless Instructor (Cisco, CWNP & Ekahau)
Content Developer for digital learning
Principal Consultant, MRN Networks
WLPC 2026 Best Content Contribution Award
Notes: I’m Rasika Nayanajith—Wireless Instructor, Content Developer, and Principal Consultant at MRN Networks… and I spend a lot of my time working with Wi‑Fi troubleshooting and analysis.
I was lucky to receive the WLPC 2026 Best Content Contribution Award—so if you were one of the people who voted, thank you… it really means a lot.

## Slide 3
Wi-Fi Analysis References
https://ieeexplore.ieee.org/browse/standards/get-program/page/series?id=68
Notes: https://ieeexplore.ieee.org/browse/standards/get-program/page/series?id=68

## Slide 4
Wi-Fi PCAP Methods
Wi-Fi Clients
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
macOS (AirTool)
Linux OS
Windows OS (CommView)
Sidos & NetAlly
Ekahau SideKick2
Cisco 9800 WLC
Cisco Catalyst Centre
Other Vendors
Multi-channel
Multi-channel
Single channel
Single channel
Sniffer mode AP
HPE Aruba/Juniper Mist
Cisco Meraki
Prof Test Tools
Multi-channel
Multi-channel
https://mrncciew.com/2025/11/05/mastering-wi-fi-packet-captures/
Remote Capture
Notes: https://mrncciew.com/2025/11/05/mastering-wi-fi-packet-captures

## Slide 5
Capture Adapters : What Matters ?
  Operating modes
    Managed vs Monitor
    PCAP requires Monitor mode
  Capabilities
    Wi-Fi 4, 5, 6, 6E, 7
    Spatial streams (SS)
  Capture strategy
    Single channel PCAP
    Multi-cahnnel (roaming analysis)
    Data vs Management/Control traffic

## Slide 6
Where to Capture Traffic ?
  Capture perspective
    Client-side vs AP-side?
    Each provides a different view
  Client behavior matter
    Roaming vs Stationary
    Roaming analysis require multi-channel PCAP
  Capture locations
    OTA: Over-the-Air( near Client or AP)
    SPAN (AP/ WLC)
    Auth Server (RADIUS)
    Load balancers

## Slide 7: Over-the-Air Capture using Endpoints (Capturing Wi‑Fi traffic directly from your laptop)

## Slide 8
Wi-Fi PCAP on mac-OS (Single Channel)
  What works?
    Built-in Wi‑Fi adapter
    Native monitor mode
    Tools: Airtool2
  Limitations
    Single-channel PCAP
    Limited support on Apple N1
  Advanced feature of AirTool2
    Multi-channel PCAP using WLANPi
    Zigbee/BLE PCAP
https://www.intuitibits.com/products/
Wi-Fi Client
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
macOS (Airtool2)
Single channel
8
Notes: https://www.intuitibits.com/products/

## Slide 9
Multi-channel PCAP with mac-OS
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
Why multi-channel
  Capture roaming events
  Avoid missing frames
How to achieve it
  Use external sensor (WLANPi)
  Airtoo2 > Multi-source capture
WLAN Pi
Multi-channel
Multi-channel
Single channel
9
Wi-Fi Client
macOS (Airtool2)
Single channel

## Slide 10
Wi-Fi PCAP on Windows
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
Windows OS
Key limitation
  No native monitor mode
How it works
  Vendor drivers (eg Tamosoft Commview)
https://www.tamos.com/download/main/ca
10
Wi-Fi Client

## Slide 11
Remote Wi-Fi PCAP on Windows
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
  WLANPi as remote capture device with Wireshark
  Enable WiFidump when installing wireshark
  Support single channel PCAP
WLAN Pi
11
Wi-Fi Client
Windows OS

## Slide 12
Wi-Fi PCAP on Linux
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
Linux OS
12
Wi-Fi Client
mrn-1X [5|6 GHz]
(WPA3-E)
  Key advantages
  Full monitor mode support
  Flexible and powerful
  Capabilities
  Single-channel capture
  Multi-channel capture
  How it works
  Create monitor mode interface
  Set channel & bandwidth
  Capture with Wireshark / tcpdump
Notes: Linux offers the most control and flexibility for Wi‑Fi packet capture

## Slide 13
Linux PCAP Commands
Identify interface
Create a ‘monitor’ mode interface
Delete ‘managed’ mode interface
Bring up the monitor mode interface
Set capture frequency
Run Wireshark & Capture traffic on monitor mode interfaces
iw phy [phy0] interface add [mrn0] type monitor
ifconfig [mrn0] up
iw dev [mrn0] set freq <control freq> [20|40|80|80+80|160] [<center1_freq> [<center2_freq>]]
iw dev
iw dev [wlan0] del
13
Notes: Linux gives full control over monitor mode and capture parameters

## Slide 14: Wi-Fi PCAP with Professional Tools (Beyond Laptop limitations)
Ekahau
NetAlly
Sidos
Notes: So far we’ve been working with laptops — and we’ve seen their limitations.
This is where professional tools come in — designed specifically for reliable and multi-channel Wi‑Fi capture.

## Slide 15
Wi-Fi PCAP with Ekahau Analyzer
https://www.ekahau.com/watch/product-news-just-go-survey-optimizer-packet-capture-and-more
Cisco CW9178I
CH1@20 [2.4GHz]
CH149@80 [5GHz]
CH21@80 [6GHz]
mrn-1X [5|6 GHz]
(WPA3-E)
mrn-PSK [2.4|5|6 GHz] (WPA3-P)
mrn-Guest [5GHz] (OWE)
Multi-channel PCAP (up to 4)
Support 2.4, 5 and 6 GHz
Require Apple iOS device (iPad/iPhone)
    Ekahau Analyzer App
Ekahau SideKick2
Multi-channel
Wi-Fi Client
Notes: https://www.ekahau.com/watch/product-news-just-go-survey-optimizer-packet-capture-and-more

## Slide 16
Wi-Fi PCAP with NetAlly
Useful in ad-hoc troubleshooting
Easy handheld device
https://www.netally.com/general/working-with-your-packets/
Notes: https://www.netally.com/general/working-with-your-packets/

## Slide 17
Wi-Fi PCAP with Sidos
https://www.linkedin.com/posts/mika-hakala-54894_sidos-microapps-26-packet-capture-app-activity-7424116631267733504-UN25
Notes: https://www.linkedin.com/posts/mika-hakala-54894_sidos-microapps-26-packet-capture-app-activity-7424116631267733504-UN25

## Slide 18: Wi-Fi PCAP using Infrastructure (Capture traffic directly from APs and controllers)

## Slide 19
Infrastructure PCAP – Pro & Cons
19
  ✅ No extra hardware
  ✅ Centralized capture & control
  ✅ Decrypted traffic (vendor dependent)
  ✅ Event-driven / automated capture
  ⚠️ AP-perspective only
  ⚠️ Limited RF visibility
  ⚠️ Vendor-dependent behavior
  ⚠️ Not true OTA capture
Notes: Infrastructure capture is very powerful — especially because you don’t need extra hardware…

## Slide 20
Wi-Fi PCAP with Sniffer AP
https://mrncciew.com/2018/04/07/Wi-Fi-captures-with-sniffer-mode-ap/
Notes: https://www.ekahau.com/watch/product-news-just-go-survey-optimizer-packet-capture-and-more

## Slide 21
Wi-Fi PCAP with 9800 WLC
Local Mode –> All traffic go to WLC
FlexConnect Mode –> Only Control Traffic go to WLC
Cisco
9800 WLC
Cisco
ISE
Cisco
Catalyst Centre
Cisco
9800 WLC
Cisco
ISE
Cisco
Catalyst Centre

## Slide 22
Wi-Fi PCAP with Cisco Meraki
Full Data Capture
Decrypted traffic view
Limit to 100k packets or 20min
https://www.ciscolive.com/c/dam/r/ciscolive/global-event/docs/2025/pdf/BRKEWN-2039.pdf
Notes: https://www.ciscolive.com/c/dam/r/ciscolive/global-event/docs/2025/pdf/BRKEWN-2039.pdf

## Slide 23
Wi-Fi PCAP with Vendors
https://mrncciew.com/2024/10/16/wi-fi-pcap-with-mist/
https://mrncciew.com/2024/10/13/wi-fi-pcap-with-unifi/
Notes: https://mrncciew.com/2024/10/16/wi-fi-pcap-with-mist/
https://mrncciew.com/2024/10/13/wi-fi-pcap-with-unifi/

## Slide 24: Struggling with PCAPs? Free tools to analyze faster and smarter
Wireshark
Wi-Fi Hawk
AI + Browser

## Slide 25
Wireshark Profiles
https://mrncciew.com/2025/09/02/get-rockstarwifi-wireshark-profile/
Custom wireshark profile (free to use)
Wi-Fi 7 Analysis included
Notes: https://mrncciew.com/2025/09/02/get-rockstarwifi-wireshark-profile/

## Slide 26
Wi-Fi Hawk
Free Cisco tool for WiFi PCAP analysis
Automated issue detection
Event Flow visualization
Excel-based reporting
Cross-platform with broad PCAP support
https://mrncciew.com/2022/08/09/cisco-wifi-hawk/
Notes: https://mrncciew.com/2022/08/09/cisco-wifi-hawk/

## Slide 27
PCAP Analysis : app.wlananalyser.com
Free & browser-based
AI-powered root cause diagnosis
Privacy-first — analysis results are held in RAM for up to 1 hour then auto-deleted
https://app.wlananalyser.com/
Notes: app.wlananalyser.com
https://shankarwifi.com/

## Slide 28: Thank you…