## Slide 1: Kiran Avva, DoE, cnWave Prabhash Dhyani, DoE, Enterprise Wi-Fi
Multi-Gigabit Wireless Fabric for Smart Cities, Logistics, and Public Access
Wi-Fi Knowledge Summit, 2023

## Slide 2: Cambium Networks - Connectivity That Just Works
Wireless fabric around the world,
  Powers reliable Connections from 2 meters to 200 Kms.
  Point-to-point, point-to-multipoint and WLAN
What can be wireless, will be wireless!
CMBM
Mission: Connect the Unconnected

## Slide 3: Smart Cities, Logistics and Public Wi-Fi Challenges
To give a seamless end-to-end connectivity to end users, backhaul should be as reliable as Wi-Fi. Backhaul should have following properties:
Cost-Effective
Flexible
Resilient
Fast
Recoverable
Fiber is expensive
Difficult Terrains
Hard to reach locations
Permissions required
Takes time
Easily deployable
Temporary Installations
Rapid Deployments Scenarios
Meet growing demands
Not easily susceptible to damage
Weather, construction work damage fiber networks.
HA is difficult with Fiber.
Comparable throughput as Fiber
Suitable for applications as video surveillance, calls
Faster recovery
Without end-user’s notice

## Slide 4: Fixed Wireless Access (FWA) Networks
300 m
5 km
10 km
Subscriber Bandwidth
Subscriber Density
200 Mbps
400 Mbps
>1 Gbps
60 GHz cnWave
cnWave 5G Fixed
3 GHz PMP 450
Tower Location
ePMP 4000 & Force 4xx
KPI |  |  | 
Technology | 802.11ay Terragraph | 5G NR | cnMedusa MU-MIMO  5G NR
Sector Capacity | > 15 Gbps | > 3 Gbps | > 1 Gbps
Subscribers per Sector | 30 | 240 | 238

## Slide 5: 60 GHz Networks Are Popping Up Everywhere

## Slide 6: 60 GHz is Proven Gbps Infrastructure
Verticals
Service Providers (WISP’s, Carriers, Fiber)
Enterprise (MDU’s, Logistics, Retail)
Industrial (Oil/Gas, Freight Rail)
Municipalities (Public Wi-Fi, City Services)
Solutions
CCTV/Video Surveillance Backhaul
Wi-Fi Backhaul
Campus Connectivity
Residential/Business Internet Access
Village of Standard, Alberta, Canada
Freight Railyard
Montreal, Canada
Pentanet Service Provider
Perth, Australia
Public WiFi Back Haul
City of San Jose, USA

## Slide 7: 60 GHz frequency band

## Slide 8: 60 GHz Propagation

## Slide 9: 802.11ad  802.11ay: What has Changed?
High Performance Over
Short Distances
802.11ad Standard
2010
Network
Capabilities
High Availability
Cloud Management
Scalability
Network Capacity
Small Cell Backhaul
Campus Area Network
Fiber Extension
Urban Network
Enterprise Private Network
Gigabit Residential Service
2020
802.11ay Standard + Terragraph
Dense Deployment
Network Efficiency
Endless Possibilities

## Slide 10: Beamforming and Directional Antennas
Due to the short wavelength of 60 GHz, antenna elements are very small in size.
This allows us to have a large phased array in a small form factor.
The technology we use is RF beamforming, and we utilize lookup tables to pre-program the phase and magnitude to define a beam direction.
The picture shows different beams we could select on the fly during the link-up process. Only one element in the phased array is illuminated.
This minimizes interference, which is quite useful in a mesh. Data is sent in a narrow beam specific to that link.

## Slide 11: Flexible Deployment Options
Point-to-Point
Sector 2
Sector 1
Distributed Network
Centralized Controller
Optimum Route Calculated at each DN
Total of 30 CN’s per DN
Management & Configuration Centralized, Reliability and Redundancy Distributed
Point-to-Multipoint

## Slide 12: Deployment Example – Building a Distributed network
V5000 DN
V1000 CN
V3000 CN
Endless Deployment Scenarios
– Auto healing
Gigabit PTP (V1000-V1000)
Long range multi-Gigabit PTP (V3000-V3000)
Mesh (DN-DN)
Sector 2
Sector 1

## Slide 13: cnMaestro: V5000 Distributed Networks

## Slide 14: TDD Synchronization
Synchronization is used to control the transmit and receive of signal to prevent self-interference
Radios assigned with same polarity will be transmitting and receiving at the same time.
  Two types of Polarity
    Odd
    Even
  When Odd nodes are Tx
  Even nodes will be Rx

## Slide 15: Layer 2 and Layer 3 Networking
Terragraph/QCA/Facebook/Cambium have studied the impact of layer 2 vs layer 3 mesh networks and settled on layer 3 for a reason.
  Layer 2 is transparent to all Ethernet traffic so can simplify deployments on a small scale
However:
  As the network grows, layer 2 broadcast traffic can overwhelm the network. Flooding can occur causing congestion and inefficiency
  Protection is required to avoid Client to Client communication, devices attached to CN’s can discover each other.
OPEN/R from Facebook provides the layer 3 routing between nodes in the mesh network.
cnWave has native layer 3 support and enables layer 2 tunnelling at the touch of a button.
Cambium cnWave aligns to the networking layer from Terragraph and differentiates with superior wireless performance and stability.
Notes:     You can imagine a broadcast storm occurring when a large number of customers come online at the same time e.g. after software upgrade or a backhaul link is re-established.
It’s easier to segment networks, restrict broadcast traffic to subnets

## Slide 16: 60 GHz cnWave Cost per node passed is 41% of Fiber
Source: Facebook Connectivity OTE Gerakas-TG-BusinessCase
cnWave plan showing wireless DN and POP locations
FTTH Plan showing: Trenches, Closures, Cabinets, Splice Points, Underground Cable
Wireless Coverage breakeven at 14 months
Fiber breakeven at 30 months

## Slide 17: Example 1: Distributed Mesh vs. Hub-and-Spoke
Real-world design example
Service Provider goal is 100% coverage of 55 homes in this neighborhood
  500Mbps/1Gbps capacity
Design constraints
  Line of sight
  < 200 meter range for high modulation
  No more than 15 CN’s per sector
Option 1:Traditional Hub/Spoke
Option 2: Distributed Mesh

## Slide 18: Example 1: Traditional Hub/Spoke
56% of buildings covered by uPOP with 10m pole
30m / 10-story tower required for 96% coverage
Southwest quadrant is already maxed out at more than 15 CN’s
Far West CN’s are at edge of range
Single tree can block several houses
No resiliency
Pole Height | Covered | Total | Percent
10m | 31 | 55 | 56%
15m | 44 | 55 | 80%
20m | 50 | 55 | 91%
25m | 52 | 55 | 95%
30m | 53 | 55 | 96%

## Slide 19: Example 1: Distributed Mesh
Mesh with 7 DNs covers 96% of homes
DN’s at 10m height
Benefits
  Reliable
    most homes covered by multiple DNs
  Performance
    links are shorter / higher modulation
    fewer CN’s per DN
  Scalable
    Room to add CN’s in each direction
    Easy to expand mesh beyond current boundaries
    Single obstructions less critical

## Slide 20: City of San Jose – Public WiFi Infrastructure

## Slide 22: Canada – Towns and Villages

## Slide 23: Private Network: Rail Yard Coverage
REQUIREMENTS
  Provide backhaul for Wi-Fi coverage and video surveillance network.
  Off load large telemetry and video data payloads (Gigabyte/Terabyte) from the train.
  SOLUTION
  Deploy 60 GHz cnWave V5000, V3000, and V1000 with Point-to-Point, Point-to-Multipoint, and Mesh configurations.

## Slide 24: Popup Networks - Concerts
Campground
Reseller: 1TOP IT
List of Material and numbers sold
  2 x V5000
  19 x Outdoor APs (E700, E510, E501S & E502S)
  Installation date
    Spring 2022

## Slide 25: cnWave Platform
V5000
V3000
Distribution Node
V1000
Client Nodes (PMP or PTP)
High Gain
Small
Form-Factor
Dual Sector
25
44.5 dBi Dish
40.5 dBi Dish
V2000
Flexible
Mid-Range
All 60 GHz cnWave products include:
  Cloud or on-premises network management with cnMaestro™
  Optional advanced management features with cnMaestro X
  Network planning capabilities with cnHeat, LINKPlanner, and ANP
  On-board or Remote e2e Controller Software
  Layer 2 or layer 3 network connectivity
  IPv4 or IPv6 networking protocols
  Security with HTTPS interfaces and 128-bit AES encryption
  3-year warranty
  Options for extended warranty, Cambium Care Pro, and advanced replacement

## Slide 26: Network Planning
LINKPlanner
  Support PTP/PMP configuration with BOM creation
cnHeat
  Using LiDAR data to create precise coverage plans
Distributed Network Planning
  Site identification and preparation
  LOS identification & optimization
  TCO/CAPEX calculations

## Slide 27: Management with cnMaestro X
Single console for the wireless fabric – Wi-Fi, Switching, 60GHz, Fixed Wireless
Simple and easy-to-navigate for fast time-to-productivity
Powerful troubleshooting tools for rapid problem resolution
Flexible integration via standard APIs with 3rd party solutions and MSP customization

## Slide 28: Cambium’s ONE Network
Integrated Network Security
APIs
Outdoor Campus
Outdoor Wi-Fi,
Multi-Gbps Wireless Backhaul
Ruggedized Switching
z
Switching
Indoor LAN
Wi-Fi
Security & SD-WAN
Planning
Deployment
Operations
Cloud Management & Analytics

## Slide 29: Application Intelligence for Predictable Performance
Wi-Fi
WAN
App Control at the WAN Edge
App Control at the Wi-Fi Edge

## Slide 30: Policy Based Automation on the Wired Network
Rule
Action
+
Policy
=
Camera Policy
Identify Camera
Place Camera on VLAN 100
ID Camera
Profile & ID device using PBA Rule
Configure Switch Port based on user defined policy for a camera
Access Point
Identify AP
Configure switch port automatically

## Slide 31: Cambium ONE Network Summary
Superior Performance
Application optimized
High density, long range
Simple to Operate
Cloud managed
Integrated automation
Economical
Less equipment
Lower TCO
ONE Network
Wi-Fi, switching, security & backhaul in one solution