## Slide 1
802.11bf
Wi-Fi Sensing &
IEEE 802.11bf
Standardizing the Invisible — From Hacks to Protocol
Chaitanya Tata · Founder & CTO · Dotstar Consulting
Notes: OPENING (1 min)
Welcome everyone to Wi-Fi KS 2026 — thank you for having me.
Before the first slide: answer "what are we sensing?" out loud. Say: "We are sensing CHANGES IN THE WIRELESS CHANNEL caused by the physical environment. Not the device. The space between devices. A person moving changes the multipath propagation of every Wi-Fi packet. We measure that change." This anchors everything that follows.
My name is Chaitanya Tata, Founder and CTO of Dotstar Consulting — a Hyderabad-based wireless engineering firm specialising in silicon-to-cloud Wi-Fi and IoT systems.
We have 20 minutes, so I'll move briskly. I'll flag each section. Save questions for the end — I'll leave 5 minutes.
REF: IEEE 802.11bf-2025 standard (available from IEEE Xplore)

## Slide 2
OVERVIEW
Talk Outline
01
History of Wi-Fi Sensing
02
How Wi-Fi Sensing Works — CSI Fundamentals
03
Proprietary Chips: Ingenuity & Limitations
04
802.11bf — The Standard That Changes Everything
05
802.11bf Deep Dive — Handshake & CSI Flow
06
CSI in Plain English — What Does Sensing Look Like?
07
Wi-Fi Alliance Sensing Certification
08
Full Pipeline — What 802.11bf Covers vs What You Build
09
What 802.11bf Doesn't Solve — Open Gaps
10
11
Technology Landscape — Full Comparison
12
Lab vs Field · Trends · Q&A
Use Cases & Beyond
Notes: AGENDA (30 sec)
Quick roadmap of what we'll cover. First half is technical foundations — if you know CSI already, mentally fast-forward. Second half is where the new material lives: 802.11bf, WFA certification, the pipeline picture, gaps, and real deployment learnings.
I'll pause briefly at slide 6 because I find it's the one slide that makes the whole topic click for non-RF people in the audience.

## Slide 3
FOUNDATION
What Are We Actually Sensing?
Not the device. Not the channel quality.
The physical space between devices.
📡 The Channel H(f,t)
Every Wi-Fi packet travels through a physical environment. Objects, walls, and people scatter, absorb and reflect it. The received channel H encodes all of that geometry — in complex numbers, per subcarrier.
🏃 Motion Changes H
A person moving 1 metre away changes H measurably within milliseconds. Even a chest expanding by 2–3 mm at 0.2 Hz (breathing) perturbs the phase of nearby subcarriers. The person IS the signal.
🎯 We Infer the Scene
By tracking HOW H changes — amplitude variance, phase slope, Doppler spectrum — we infer presence, motion, gesture, or vital signs. No camera. No contact. No extra hardware.
802.11bf standardises HOW devices exchange H measurements. What you do with them is still your engineering problem.
Notes: WHAT ARE WE SENSING? (30 seconds — say this before ANY technical content)
This slide sets the frame for the entire talk. If people leave understanding only one thing, it should be this.
Say it slowly:
"We are not sensing the Wi-Fi device. We're not measuring signal quality or throughput. We are using the radio channel BETWEEN devices as a distributed sensor for the physical environment. A person, an object, a breathing chest — they all change how radio waves bounce around the room. We measure those changes."
This prevents the most common misconception: that Wi-Fi sensing is about measuring packet loss or RSSI. It has nothing to do with data quality. The channel could be perfect for data and still carry rich sensing information.
WHY THIS MATTERS FOR THE TALK:
- When you later say "the CSI matrix is contaminated by RFIC impairments" — they'll understand what "clean sensing signal" means
- When you say "model trained in one room fails in another" — they'll understand why (the physical geometry changes H differently)
- When you say "privacy preserving" — they'll understand that there's no image, only a mathematical abstraction of geometry

## Slide 4
SECTION 01 — HISTORY OF WI-FI SENSING
History of Wi-Fi Sensing
2002
MIT Lincoln Lab's DETO — radar-inspired passive RF sensing research begins
2008
WiSee / Soli predecessors — gesture recognition via Doppler shifts
2011
FILA & PADS: first published CSI-based indoor localization papers
2015
WiGest (Abdelnasser et al., INFOCOM) — gesture recognition with commodity Wi-Fi NIC
2015–18
Academic explosion — breathing detection, fall detection, people counting
2017
Proprietary commercial chips: Cognitive Systems (Aura), Aerial
2020
IEEE TGbf task group formed — standardization begins
2025
IEEE 802.11bf ratified — 26 September 2025 ★
Notes: HISTORY — DETAILED TALKING POINTS PER ERA
2002 — MIT Lincoln Lab (DETO): The origin. Researchers proved that background radio waves — TV and radio signals — could passively track moving targets without a dedicated radar transmitter. Military-grade passive bistatic radar research. Key insight: the environment IS the sensor.
2008 — WiSee Precursors: Transition to consumer radio. Early Wi-Fi transmissions carried enough Doppler information to track coarse body movement — walking, arm swings. Macro-Doppler only; CSI was not yet in scope.
2011 — FILA & PADS (The CSI Revolution): The critical inflection. Prior work used RSSI — a single scalar. FILA and PADS introduced Channel State Information (CSI) — hundreds of complex values per packet — for indoor localisation. This is the moment modern Wi-Fi sensing was born.
2015 — WiGest (Abdelnasser et al., INFOCOM): The democratisation moment. Gesture recognition on a commodity Intel 5300 NIC using a patched open-source driver. No lab hardware. Anyone with a laptop and a $50 NIC could replicate it. This opened the academic floodgates.
2015–18 — Academic Explosion: Sensing branched from motion into micro-vitals. Breathing detection (phase at 0.2–0.3 Hz), fall detection (Doppler spike), device-free crowd counting. Papers from CMU, MIT, Peking University, NTU dominated this era.
2017 — Commercial Pioneers: Cognitive Systems (Aura) and Aerial began embedding sensing into mesh routers via proprietary firmware, licensing to ISPs — Plume, Eero. This created the "your router is already watching you" reality that predates 802.11bf.
2020–25 — Standardisation: TGbf formed, 400+ contributions, 4 years to ratification. September 26, 2025: 802.11bf-2025 published. A 20-year cycle from passive radar experiment to open global standard.
REFS:
- Abdelnasser et al. (2015) WiGest — IEEE INFOCOM
- Halperin et al. (2011) Intel 5300 CSI Tool — ACM SIGCOMM CCR
- IEEE 802.11bf-2025: https://standards.ieee.org/ieee/802.11bf

## Slide 5
SECTION 02 — HOW WI-FI SENSING WORKS
How Wi-Fi Sensing Works
RF Multipath Environment
Every object reflects, absorbs, and scatters Wi-Fi signals. Moving objects alter the multipath propagation profile in real-time. The channel itself becomes a distributed sensor — no additional hardware needed.
CSI vs RSSI
RSSI is a single scalar. CSI (Channel State Information) exposes per-subcarrier complex amplitude & phase: H[Nrx × Ntx × Nsc] per packet — typically 200+ independent measurements per frame.
Sensing Signal Chain
Tx NDP → air channel H(f,t) perturbed by scene → Rx captures CSI matrix → feature extraction (FFT, Doppler, PCA) → ML/DSP inference → human-interpretable output (presence, vitals, gesture).
Notes: HOW IT WORKS (1.5 min)
The key intuition: a Wi-Fi channel is not a clean pipe — it's a fingerprint of the physical environment. Every multipath bounce encodes spatial information.
RSSI gives you one number: "signal strength". CSI gives you hundreds of complex numbers — one per OFDM subcarrier — each capturing how a slightly different frequency experienced the channel. A person breathing 1 metre away creates a periodic perturbation across those subcarriers at 0.2–0.3 Hz.
Think of it as an acoustic sonar, but using radio waves, and the "sonar" device is already in every home.
REFS:
- Guo, L. et al. (2019) "A Survey on Channel State Information-Based Sensing for IoT Applications" — IEEE IoT Journal
- Yang, Z. et al. (2013) "From RSSI to CSI: Indoor Localization via Channel Response" — ACM Computing Surveys

## Slide 6
SECTION 02 — HOW WI-FI SENSING WORKS
Channel State Information (CSI): The Sensing Primitive
802.11ax/bf uses 234 data subcarriers at 20 MHz. SMR reports Ng-grouped HE-LTF estimates — not one per subcarrier. At Ng=4: ~60 groups/stream.
TX1→ [H₁₁|∠φ₁₁] [H₁₂|∠φ₁₂] ... [H₁ₙ|∠φ₁ₙ] →RX1
TX2→ [H₂₁|∠φ₂₁] [H₂₂|∠φ₂₂] ... [H₂ₙ|∠φ₂ₙ] →RX2
TX3→ [H₃₁|∠φ₃₁] [H₃₂|∠φ₃₂] ... [H₃ₙ|∠φ₃ₙ] →RX3
3D
Tensor
Time × Subcarriers × Pairs
20–200
Hz CSI rate
Up to 1kHz theoretical
~60–250
SMR groups Ng=4
Physical 234–996 · Ng-grouped
Motion changes H in real-time → track |H| and ∠H → presence, vitals, gesture.
How the HE-LTF extracts H:
L-STF
L-LTF
HE-SIG
HE-LTF
×N
NDP
(empty)
▲ H extracted here
1
Known pilot transmitted
HE-LTF sequence known to both TX and RX. Sensing NDPs append N extra LTF symbols for better SNR.
2
Receiver correlates
Cross-correlate received LTF vs known: H̃ = y/x per subcarrier per antenna pair. Solves the channel in one division.
3
H matrix delivered
Each packet produces H[Nrx×Ntx×Nsc]. Stack packets over time → 3D tensor. Motion changes H measurably within milliseconds.
SMR spec: §9.4 / Table 9-129l — 8-bit I + 8-bit Q per Ng group · Ng=4 mandatory
Notes: CSI PRIMITIVE — what this slide must convey
LEFT SIDE:
The H matrix is what we get from every Wi-Fi packet. For each TX-RX antenna pair, we get a complex number (amplitude |H| and phase ∠φ) for each subcarrier. At 20 MHz with Ng=4, that is ~60 groups per pair. With 2×2 MIMO that is 240 complex numbers per packet at 20–200 Hz.
The three stat numbers tell the story quickly: 3D (it is a tensor, not a scalar), 20–200 Hz (the update rate), ~60–250 groups (the resolution at Ng=4).
RIGHT SIDE:
The HE-LTF (High Efficiency Long Training Field) is the part of the Wi-Fi frame where channel estimation happens. The receiver knows exactly what sequence was transmitted. It correlates the received signal against the known sequence to solve for H. Sensing NDPs add extra LTF symbols to improve the estimate quality.
The three steps are the full story: TX sends known pilot → RX correlates → H matrix delivered to the sensing application.
REFS:
- Halperin et al. (2011) — Intel 5300 CSI tool paper, ACM SIGCOMM CCR
- 802.11bf-2025 Section 9.4 — CSI measurement report format

## Slide 7
SECTION 02 — HOW WI-FI SENSING WORKS
What Does Sensing Actually Look Like?
Same 802.11bf CSI stream — three inferences — zero cameras, zero contact
USE CASE A: Presence Detection
CSI amplitude variance over time →
Empty room:
NO
PERSON
Person present:
YES
PERSON
How: Variance of CSI amplitude across subcarriers. Empty room → near-flat. Human body → elevated variance from micro-motion and RF absorption. Threshold-based in controlled conditions — ML needed for real-world robustness.
USE CASE B: Breathing Rate
CSI phase variance — 30-second window:
← 30 sec →
15
BPM
After 0.1–0.5 Hz bandpass + FFT:
Peak at 0.25 Hz = 15 breaths/min
How: Chest expansion ~0.2–0.3 Hz modulates subcarrier phase. Bandpass → FFT → dominant peak = breathing rate.
USE CASE C: Fall Detection
CSI Doppler Spectrogram (STFT) — 5-second sliding window:
← 5 seconds → ← stillness (0 Hz)
Hi freq
Lo freq
⚠ FALL DETECTED — CRITICAL EVENT
How: STFT slices the CSI stream into overlapping windows. Maps velocity (Doppler freq) vs. time. Sudden broadband spike → abrupt 0 Hz stillness = unmistakable fall signature. Action → sudden acceleration. Effect → broadband RF Doppler burst. Tool → STFT time-localises the event.
Notes: PLAIN ENGLISH — KEY SLIDE (1.5 min)
LEFT PANEL: I have a Wi-Fi packet going across the room. If the room is empty, the CSI amplitude variance is nearly flat — stable multipath, nothing changing. The moment a person walks in, variance spikes. Even a still person breathing creates micro-perturbations. This is a YES/NO answer from a threshold comparison — no machine learning, no training data.
RIGHT PANEL: Same stream. I apply a 0.1–0.5 Hz bandpass filter (that's the human breathing frequency range), then run an FFT. The peak in the frequency domain tells me breathing rate. 14 BPM readout on a chip that cost $3, already in your home.
This is why I find 802.11bf exciting — we're turning infrastructure that's already deployed into a sensor network.
REFS:
- Liu, J. et al. (2015) "Tracking Vital Signs During Sleep Leveraging Off-the-Shelf WiFi" — ACM MobiHoc
- Wang, H. et al. (2016) "TensorBeat: Tensor Decomposition for Monitoring Multi-Person Breathing Beats with Commodity WiFi" — ACM TIST

## Slide 8
SECTION 03 — PROPRIETARY CHIPS
Proprietary Sensing Chips — Ingenuity & Limits
📡 Already in your router — 802.11bf = interoperability, not invention.
Origin AI: 100M+ deployments · Plume / Eero ISP gateways
Cognitive Systems (Aura)
802.11ac FW mod · CSI via backdoor driver APIs · proprietary motion event API
Aerial → Qualcomm
Custom beacon injection · Wi-Fi 6E sensing packets · closed reporting format
Academic toolkits
Intel 5300 iwlwifi patch · Atheros CSI Tool · Nexmon BCM · out-of-tree kernel patches
⚠ Why Proprietary Approaches Failed to Scale
Vendor lock-in
Cognitive/Qualcomm/Broadcom stacks: zero interoperability
Driver fragility
Out-of-tree patches break on every kernel update
No protocol
Responder must be same chip family; generic AP/STA excluded
Phase inconsistency
Normalization varies by die rev, AGC state, temperature
Regulatory gap
No coexistence standard — interference with normal traffic
Notes: PROPRIETARY CHIPS (1 min)
The Intel 5300 CSI tool was the academic workhorse from 2011 to about 2018. You can download the patched iwlwifi driver from Daniel Halperin's GitHub. But good luck running it on a 2024 kernel.
The core problem: none of these systems could talk to each other. If I have a Qualcomm AP and a Broadcom STA, there's no sensing. 802.11bf fixes exactly this.
REFS:
- Cognitive Systems Aura: https://cognitivesystems.com/
- Nexmon CSI tool: https://github.com/seemoo-lab/nexmon_csi
- Dhalperi Intel CSI tool: https://github.com/dhalperi/linux-80211n-csitool

## Slide 9
SECTION 04 — 802.11bf STANDARD
IEEE 802.11bf
Wi-Fi SENSING — The Standard
Sep 2025
Standard Ratified
TGbf
Task Group (est. 2020)
Sub-7 GHz
+ 45/60 GHz
Frequency coverage
802.11az
NDP-based ranging cousin
What problem does 802.11bf solve?
802.11bf standardizes sensing session establishment (SI/SR roles), CSI measurement reporting format, beamforming feedback for sensing, and coexistence rules with legacy traffic. Wi-Fi sensing goes from chip vendor trade secret to universally implementable open protocol.
Notes: 802.11bf INTRO (1 min)
September 26, 2025 — the standard is published. This is the payoff slide.
TGbf ran for 4 years. Over 400 technical contributions from companies including Intel, Qualcomm, Broadcom, Huawei, Ericsson, Apple, Samsung. It went through multiple drafts.
The standard covers Sub-7 GHz (the 2.4/5/6 GHz bands you already use) and 45/60 GHz mmWave (higher resolution, shorter range). It references 802.11az for ranging/NDP concepts.
Key thing to communicate: this doesn't require new hardware in many cases. An 802.11ax (Wi-Fi 6) AP with updated firmware can be 802.11bf compliant.
REFS:
- IEEE 802.11bf-2025: https://standards.ieee.org/ieee/802.11bf/7451/
- TGbf status page: https://www.ieee802.org/11/Reports/tgbf_update.htm
- Lacatus, C. et al. (2022) "IEEE 802.11bf: Toward Ubiquitous Wi-Fi Sensing" — IEEE Communications Magazine

## Slide 10
SECTION 05 — HANDSHAKE & CSI FLOW
802.11bf — Standardized Handshake & CSI Flow
SENSING
INITIATOR (SI)
SENSING
RESPONDER (SR)
▶
① Sensing Measurement Setup Request (SMSR) — specifies type, periodicity, Nsc grouping
▶
② Sensing Measurement Setup Response — capability ACK
▶
③ NDP / Sensing Frame — triggers CSI collection at SR
▶
④ Sensing Measurement Report (SMR) — H[Nrx×Ntx×Nsc] matrix
▶
⑤ ACK + repeated measurements at configured periodicity
▶
⑥ Sensing Measurement Instance Termination (SMIT)
Key Points
• MIMO CSI per stream
• Sub-7 GHz & mmWave
• Coexists w/ legacy STAs
• No PHY modification
• Unassociated sensing
• Privacy/consent bits
Notes: HANDSHAKE (1 min)
Walk through this carefully — it's the core of 802.11bf.
The Responder (typically the STA) acknowledges and confirms capability. Then the NDP exchange begins — Null Data Packets carry no payload but traverse the full channel, so the Responder can extract a precise CSI estimate.
The SMR comes back: a full complex H matrix. This is what your application layer receives. Everything below this line is standardised by 802.11bf. Everything above — what you do with the matrix — is still your problem.
SMIT terminates the session cleanly, freeing channel resources.
Key addition vs proprietary approaches: unassociated sensing (Phase 2 of 802.11bf) — a device can perform sensing before association, enabling new deployment scenarios.
REFS:
- IEEE 802.11bf-2025, Section 11 (Sensing procedures)
- Lacatus et al. (2022) IEEE Comms Magazine — good protocol walkthrough

## Slide 11
SECTION 05 — HANDSHAKE & CSI FLOW
802.11bf in Action: A Walkthrough
Scenario: A smart home AP wants to detect if a baby is left in a car seat in the living room.
STEP 1: SENSING SETUP
AP broadcasts Sensing Measurement Setup frame:
• Sensing Type: Bistatic (AP=initiator+TX, IoT Camera=receiver)
• Periodicity: 50 ms (20 Hz update rate)
• Channel: 5 GHz, 80 MHz bandwidth (→ 996 physical subcarriers)
• Duration: 10 NDP bursts per measurement window
STEP 2: POLLING & SOUNDING
AP → NDPA → IoT Camera (receiver configured)
AP → I2R NDP → IoT Camera captures channel via 2x HE-LTF symbols
SMR output: ~249 Ng=4 groups × 16 streams (80 MHz)
STEP 3: REPORTING
IoT Camera → Sensing Measurement Report → AP
Payload: Quantized amplitude |H| and phase ∠H per subcarrier/stream
Format: Standardized 802.11bf CSI Report IE (vendor-neutral parsing)
STEP 4: INFERENCE (Edge AI on AP)
Input: ~249 groups × 16 streams × T samples | Preprocess: Hampel → STFT
Model: CNN-LSTM edge-optimized <50MB
Output: Occupant yes / Breathing: 32/min / No motion
Sensing Configurations
Bistatic ✓
AP(SI/TX) + STA(SR/RX) — the primary Sub-7 GHz mode. Separate TX and RX required; full-duplex not supported on commodity silicon.
Multistatic ✓
One TX, multiple RX nodes — enables multi-AP triangulation. Future certification scope.
Monostatic
Single device TX+RX. 802.11bf defines it but ONLY for DMG/EDMG (60 GHz). NOT in Sub-7 GHz WFA certification — commodity Wi-Fi chips cannot TX and RX simultaneously.
Coordinated
SI schedules multiple monostatic devices. 802.11bf defines it for DMG. Not applicable to Sub-7 GHz commodity devices.
SMR Reporting — Sub-7 GHz
• Full H matrix (I+Q):
8-bit real + 8-bit imag per Ng group
• Ng grouping:
Ng=4 mandatory · Ng=1,2,16 optional
• Protected SMR:
Encrypted (security, not compression)
• Spec ref:
§9.4 / Table 9-129l / §11.21.6
Notes: WALKTHROUGH (1 min)
Walk the STEPS on the left — this is the complete 802.11bf session from AP perspective:
Step 2: The NDP sounding — the AP fires NDPs, the camera measures the channel.
Step 3: The SMR comes back — standardized format, any 802.11bf device can parse it.
Step 4: Inference — this is YOUR layer, not the standard's. STFT (Short-Time Fourier Transform) is the key preprocessing step after CFO/SFO removal.
Right panel — SENSING CONFIGURATIONS:
These are the four topologies 802.11bf defines:
- Bistatic: the ONLY practical Sub-7 GHz topology for commodity Wi-Fi. AP is SI/TX, STA is SR/RX. Full-duplex (simultaneous TX+RX on the same device) is not supported on standard Wi-Fi silicon. ALL WFA Sensing certification requirements are for bistatic operation.
- Multistatic: one TX, multiple RX — theoretically extends to multi-AP sensing. Not yet in WFA cert but architecturally sound.
- Monostatic: 802.11bf defines it but ONLY for DMG/EDMG (60 GHz mmWave). A single device doing TX+RX is feasible at 60 GHz with the narrow beamwidth. NOT in Sub-7 GHz WFA certification, and NOT what off-the-shelf routers and phones do. Do NOT list this as a general 802.11bf capability — your colleague is correct.
- Coordinated: defined in 802.11bf for scheduling multiple monostatic devices. Again, DMG/EDMG context. Not relevant to Sub-7 GHz commodity devices.
SMR REPORTING — Sub-7 GHz (§9.4 Table 9-129l):
The 802.11bf standard defines ONE report type for sub-7 GHz: the full H[Nrx×Ntx] complex matrix (8-bit I + 8-bit Q per subcarrier group). "Compression" is achieved via Ng grouping only: Ng=4 (mandatory), Ng=1/2/16 (optional). There is no amplitude-only, PDP, or differential quantization mode for sub-7 GHz in the ratified standard — those were DMG/60GHz candidate features discussed during TGbf standardisation (pre-2025). The slide has been corrected to reflect what is actually in the published standard.
REFS:
- 802.11bf-2025 Section 9.4 (SMR frame), Section 11.55 (sensing procedures)

## Slide 12
SECTION 05 — HANDSHAKE & CSI FLOW
SMR Payload: Encoding, Fields & Reconstruction
When the Sensing Responder (SR) sends a Sensing Measurement Report (SMR), the CSI is encoded as a compact binary payload. Here is the complete field-by-field breakdown.
SMR CSI Payload Structure — per Tx→Rx pair (from §9.4 / Table 9-129k)
Field | Size | Scope | Meaning / Engineering Significance
Scaling Factor | 12 bits | Per Tx-Rx pair | Global amplitude multiplier. True amplitude = ScalingFactor × ¦I+jQ¦. Signed, stored as a 12-bit fixed-point value.
Padding | 0 or 4 bits | If odd # of pairs | 4-bit pad inserted after last scaling factor when number of Tx-Rx pairs is odd. Aligns to byte boundary.
I (Real part) | 8 bits / group | Per Ng subcarrier group | Signed 8-bit integer. Quantised real component of H̃ after LTF correlation and Ng averaging.
Q (Imaginary part) | 8 bits / group | Per Ng subcarrier group | Signed 8-bit integer. Quantised imaginary component. Together I+jQ gives magnitude and phase.
Step-by-step Reconstruction Pipeline
1
Parse SMR payload
Extract 12-bit ScalingFactor per Tx-Rx pair, then read N×(8+8) I/Q bytes (N = floor(Nsc/Ng))
2
Reconstruct complex H̃
H̃[k] = I[k] + j·Q[k] for each Ng group k (k = 0 … N-1)
3
Apply Scaling Factor
H_scaled[k] = ScalingFactor × H̃[k]
4
Apply RX_OP_GAIN
H_true[k] = RX_OP_GAIN × H_scaled[k] ← from STF, not in SMR; must be logged by driver
5
Calibrate & stack
Remove SFO/CFO artefacts → stack packets over time → 3D tensor [time × freq × spatial]
Data Volume Calculator
Config:
2×2 MIMO, 20 MHz, Ng=4, 100 Hz
Groups/pair:
floor(242/4) = 60
Bytes/SMR:
4 pairs × [12-bit scale + 60×2 bytes] = ~486 B
Throughput:
~48 KB/s (just CSI, before headers)
@ 160 MHz:
~3.8× more → ~180 KB/s (Ng=4)
@ 320 MHz EHT:
~960 groups → ~384 KB/s
Why Ng Grouping? — Resolution vs. Bandwidth Tradeoff
Ng=1: Full subcarrier resolution (242 groups at 20 MHz) — highest spatial / Doppler fidelity, largest SMR.
Ng=4: Mandatory minimum. 60 groups at 20 MHz — 75% size reduction, still sufficient for presence + vitals.
Ng=16: Coarse (15 groups) — IoT-class only. Very low SNR use cases.
Ng=4 is the mandatory minimum for WFA Sensing certification. SI negotiates Ng in the SMSR setup frame.
Ref: IEEE 802.11bf-2025 Table 9-129k · §9.4.2 SMR format · WFA MRD 1.0 §5.3
Notes: CSI SMR FORMAT (1 min)
Walk the table left to right: each Tx-Rx pair gets a 12-bit scaling factor first. Then for each Ng group, 8-bit I + 8-bit Q. At Ng=4 and 20 MHz, that is 60 groups.
The data volume calculation is important for system design:
- At 100 Hz CSI rate with 2x2 MIMO at 20 MHz: ~48 KB/s. Manageable.
- At 160 MHz: ~180 KB/s. Still OK for a wired edge server.
- At 320 MHz EHT: ~384 KB/s. Start thinking about compression.
COMMON MISTAKE: Engineers often forget step 4 — applying RX_OP_GAIN. The SMR payload gives you ScalingFactor x (I+jQ), but without the RX_OP_GAIN from the driver, you are comparing apples to oranges across packets where AGC changed.
Ng=4 is mandatory minimum for WFA certification. Ng=1 (full subcarrier resolution) is optional and useful for research.
Refs: IEEE 802.11bf-2025 §9.4 Table 9-129k · WFA MRD 1.0 §5.3

## Slide 13
SECTION 05 — HANDSHAKE & CSI FLOW
HE Preamble Chain: From STF to CSI Extraction
Every 802.11bf sensing NDP follows the HE preamble chain below. RX_OP_GAIN is populated by the STF — not the LTF. Channel estimation H starts only at HE-LTF.
L-STF
L-LTF
L-SIG
HE-SIG-A
HE-STF
HE-LTF 1
HE-LTF…N
NO DATA
Legacy Preamble
(backward compat / coexistence)
Tells RX
LTF count
★ AGC settled
RX_OP_GAIN locked
H matrix extraction
Starts here
No payload
(NDP)
★ RX_OP_GAIN — From STF, Not LTF
The HE-STF allows the receiver's AGC (Automatic Gain Control) to settle before the LTF arrives. The final AGC register value is called RX_OP_GAIN and is stored per packet.
This gain must be applied to the raw I/Q values in the SMR to reconstruct the true channel amplitude. Without it, two packets with different gain settings are not amplitude-comparable.
Note: HE-LTF can be repeated (HE-LTF×N) — each repetition improves SNR via coherent averaging. The number of LTF symbols is signalled in HE-SIG-A. For MIMO, each spatial stream gets its own LTF sequence with orthogonal P-matrix coding so streams are separable at the receiver.
CSI Reconstruction Pipeline (Table 9-129k)
If writing code to ingest an SMR payload:
True Real Channel ∝ RX_OP_GAIN × Scaling Factor × (I + jQ)
• RX_OP_GAIN: per-packet AGC register value (from STF)
• Scaling Factor: 12-bit field in SMR (per Tx-Rx pair)
• I + jQ: 8-bit signed values per Ng group (Ng=4 mandatory)
For MIMO: each Tx-Rx antenna pair has its OWN ScalingFactor header + I/Q stream. A 2×2 system = 4 pairs = 4 scaling factors + 4 × 60 groups at 20 MHz.
HE-LTF repetitions (HE-LTF×N): The N repetitions are averaged in hardware at the receiver to improve SNR. Final H matrix is still Nrx × Ntx × Nsc — the averaging is transparent to the SMR consumer.
Notes: PREAMBLE CHAIN — DEEP DIVE (1 min)
This is the frame structure of every 802.11bf sensing NDP — walk left to right.
KEY POINT 1 — RX_OP_GAIN is from HE-STF, not HE-LTF:
The HE-STF is specifically designed for AGC training. By the time the HE-LTF arrives, the gain is locked. The RX_OP_GAIN register value tells you how much the baseband amplified the received signal. Without correcting for this, you cannot compare amplitude across packets if the AGC stepped between them.
KEY POINT 2 — The reconstruction equation:
H_true = RX_OP_GAIN x ScalingFactor x (I + jQ)
This is the pipeline any 802.11bf driver must implement. The I and Q are in the SMR payload. The ScalingFactor is also in the SMR. But RX_OP_GAIN is NOT in the SMR — it must be captured by the driver from the hardware AGC register at receive time.
KEY POINT 3 — NO DATA:
The sensing NDP has zero payload bytes after the LTF symbols. It is a preamble-only frame. This is why it is called a Null Data Packet.
Refs: IEEE 802.11bf-2025 §9.4 Table 9-129k · §27.3.11 HE-LTF · WFA MRD 1.0

## Slide 14
SECTION 05 — HANDSHAKE & CSI FLOW
Non-Trigger-Based vs Trigger-Based Sensing
802.11bf defines two MAC-layer sensing modes that differ in how uplink scheduling, OFDMA access and power management are handled.
Non-Trigger-Based (Non-TB)
AP sounds one client at a time, sequentially.
① Setup Phase
SMSR → SMSR Response
SI/SR capabilities, Ng, periodicity negotiated
② NDPA Sounding Phase
AP sends NDPA (announces sensing NDP)
NAV/TXOP set — medium reserved for full exchange
③ NDP Transmission
AP sends sensing NDP (HE-LTF payload)
SR extracts H matrix from LTF correlation
Single-client, full-BW per slot (time division)
④ Reporting Phase
SR sends SMR back to SI
Contention via EDCA — NOT strictly scheduled
Sampling jitter risk if channel contested
⑤ Termination
SMIT — session ends or repeats at next periodicity
⚠ Report uplink via EDCA — scheduling jitter degrades phase consistency
Trigger-Based (TB) Sensing
AP coordinates multiple clients simultaneously via OFDMA.
① Setup + Poll Phase
SMSR negotiation + polling frame
AP inventories active STA capabilities
② NDPA Sounding Phase
AP sends NDPA + sets TXOP/NAV
Contention-free medium guaranteed
③ TF Sounding Phase
AP sends Trigger Frame (TF)
Assigns RUs to STA-A, STA-B, STA-C
All clients uplink simultaneously (OFDMA)
SIFS-scheduled — zero MAC jitter
④ Reporting Phase
Clients send TB-NDP uplink in OFDMA
AP measures all CSI in single symbol window
Deterministic timing — phase preserved
⑤ Termination
SMIT — session ends or repeats at wake window
✓ Uplink TB-NDP at SIFS after TF — deterministic, jitter-free, power-efficient
Feature | Non-Trigger-Based | Trigger-Based
Medium Protection | TXOP / NAV in NDPA header | TXOP / NAV in Trigger/NDPA header
Slot Allocation | Implicit / chronological (NDPA order) | Explicit / dynamic (RUs in TF)
Uplink Channel | Single client, full BW — time division | Multi-client OFDMA — frequency division
MAC Jitter | EDCA contention for report uplink | SIFS-locked, deterministic (16 μs)
Power Save | Client waits for unannounced NDP | Sleeps until RSTA Availability Window opens
Best for | Simple home / 2-STA bistatic setups | Enterprise multi-static, tracking, MIMO
Ref: IEEE 802.11bf-2025 Fig. 11-108e — TB sensing measurement exchange (polling + NDPA + TF sounding + reporting phases)
Notes: NON-TB vs TB SENSING (2 min)
This is one of the most important architectural choices in 802.11bf.
NON-TB: The AP sounds one client at a time. Think of it as TDM — time division. The SMR comes back over EDCA, which means if the channel is congested, the report can be delayed. Phase coherence across packets is then corrupted — and phase is EVERYTHING for vital signs sensing.
TB (TRIGGER-BASED): The AP sends a Trigger Frame that assigns Resource Units to multiple clients. They all transmit their uplink CSI simultaneously in OFDMA. The AP receives ALL of them in one hardware window. The timing discipline is SIFS — 16 microseconds. This eliminates MAC-layer scheduling jitter entirely.
FOR ENTERPRISE: If you are doing multi-static sensing in a conference room with 4 STAs acting as SRs, TB sensing is the only viable option. Non-TB would require 4 sequential rounds — 4x the airtime, 4x the jitter opportunity.
THE TXOP POINT: In both modes, once the AP wins the medium (via EDCA/CCA), the entire sensing exchange is contention-free inside the TXOP. The difference is what happens WITHIN that TXOP.
Refs: IEEE 802.11bf-2025 Fig. 11-108e · §11 MAC procedures

## Slide 15
SECTION 07 — WFA SENSING CERTIFICATION
Wi-Fi Alliance — Sensing Certification
The Certification Journey
PHASE 1
Standard
Published
IEEE 802.11bf-2025
Sep 2025
PHASE 2
WFA Board
Approved
Apr 2026
PHASE 3
Cert Launch
Target
December 2027
PHASE 4
Ecosystem
Flywheel
Interop at scale
→
→
→
What the certification program means (public facts):
Hardware prerequisite
Wi-Fi 6 (802.11ax) certification required for all devices — no new PHY or spectrum. Existing chips can be firmware-upgraded.
Interoperability guarantee
Certified AP + certified STA from different vendors must establish a sensing session — the fundamental fragmentation problem 802.11bf solves.
4 device profiles
AP · STA · Mobile AP · 20 MHz-only STA. Each has different sensing role requirements. Wi-Fi 7 devices get expanded mandatory capabilities.
No certified product yet
Standard ratified Sep 2025. Board approved Apr 2026. First certified products expected after December 2027 cert launch.
Standard done. Chips capable. Cert window: December 2027. The teams building expertise now own the deployment wave.
Notes: WFA CERTIFICATION — PUBLIC FACTS ONLY
PUBLIC FACTS:
- IEEE 802.11bf-2025 ratified September 2025
- WFA board approved sensing certification program April 2026 (public press release)
- December 2027 certification launch target (publicly stated by WFA)
- 4 device profile categories (public)
- Wi-Fi 6 prerequisite (public)
IF ASKED FOR DETAILS IN Q&A: "The WFA has a detailed certification specification. Happy to discuss technical aspects that are public in the 802.11bf standard itself."
REFS: https://www.wi-fi.org/discover-wi-fi/wi-fi-sensing

## Slide 16
SECTION 08 — FULL PIPELINE
Full Sensing Pipeline — What the Standard Covers
APPLICATION LAYER
Presence · Fall detection · Vital signs · Gesture · Pose estimation
YOU BUILD
INFERENCE / ML
Feature engineering · Model training · Domain adaptation · Post-processing
YOU BUILD
FEATURE EXTRACTION
FFT · Doppler shift · PCA/SVD · MUSIC algorithm · AoA/ToF derivation
YOU BUILD
CSI REPORTING (SMR)
802.11bf: H[Nrx×Ntx×Nsc] matrix from baseband channel estimator (vendor-processed, not raw ADC) · amplitude · phase · per stream
802.11bf ✓
SENSING SESSION
802.11bf: SMSR/SMSR-Resp · NDP exchange · SMIT termination · coexistence
802.11bf ✓
Integrator /
App layer
IEEE 802.11bf
Notes: PIPELINE (1.5 min)
GREEN (802.11bf covers):
- The SESSION layer: how two devices agree to do sensing, how frequently, how many streams, when to stop, and how to coexist with data traffic on the same channel
- The REPORTING layer: the format of the CSI measurement report — the H matrix — so that any 802.11bf receiver can parse it, regardless of chipset
ORANGE/YELLOW (you build):
- FEATURE EXTRACTION: how you process that H matrix is entirely your choice. Doppler FFT, MUSIC algorithm, PCA decomposition — all valid, none standardised
- INFERENCE/ML: your model, your training pipeline, your domain adaptation strategy
- APPLICATION: what you actually do with the inference output
So 802.11bf solves the "plumbing" problem. The "intelligence" problem is still wide open — and frankly, that's where Dotstar Consulting plays.
This is also why the WFA certification covers only the bottom two layers — they can only certify what the standard defines.
REFS:
- 802.11bf standard architecture: Section 4 (Architecture overview)
- Pallaprolu, S.C. et al. (2022) "OFDM Radar with LTE Waveforms: An Efficient Tool for Joint Radar-Communications" for feature extraction comparison

## Slide 17
SECTION 09 — OPEN GAPS
What 802.11bf Doesn't Solve — Open Gaps
ML / Inference Layer
Standard defines the pipe, not what flows through it. Every vendor builds proprietary models — and there's no way to test if a model is failing without ground truth in the deployment environment.
Silent Failure / Generalisation
A model trained in one room degrades silently in another after furniture rearrangement. A presence detector that stops working is worse than no system. No standard for calibration metadata, retraining triggers, or domain adaptation.
Multi-AP Fusion
No protocol for time-synchronised CSI fusion across multiple APs — essential for full-room coverage and accurate person counting.
Privacy — Passive Sensing Gap
PASN provides one-time session consent — no continuous revocation. Crucially: passive RF sensing using ambient Wi-Fi transmissions (outside 802.11bf) is completely unaddressed by the standard.
Baseband Normalisation
CSI in the SMR is baseband-processed channel estimates, not raw ADC. Different chipsets implement channel estimation differently — two certified APs give different H matrices for the same physical channel.
Secure LTF — Explicitly Disabled in 802.11bf
802.11bf §27.2.2/§36.2.2 mandates SECURE_LTF_FLAG=0 in all sensing NDPs. sLTF (used in 802.11az for anti-spoofing) is prohibited — it introduces a hardware-level phase penalty that breaks compatibility with 320 MHz EHT sounding needed for high-resolution sensing. Passive RF privacy requires a different approach.
802.11bf is protocol-interoperable: the handshake, SMR format, and session negotiation work across vendors. But in a multistatic deployment, CSI matrices from different vendor chipsets use different baseband normalisation and phase references — they cannot be fused into a joint H-matrix for sensing. 802.11bf defines no cross-vendor CSI calibration baseline.
Algorithmic Interop — The Hidden Gap
Notes: GAPS — WHAT 802.11bf DOESN'T SOLVE
ML / Inference Layer: The standard delivers the CSI pipe, nothing about what features to extract or which model to use. Every vendor builds proprietary inference with zero interoperability. A sensing app certified on one vendor's implementation may fail silently on another's.
Silent Failure / Generalisation: A presence detection system that stops working after a couch is moved and gives a false "nobody home" is worse than no system. No standard for calibration metadata, retraining triggers, or domain adaptation. This is why Wi-Fi sensing has not entered safety-critical applications.
Multi-AP Fusion (three mitigations being worked on):
A. Multi-Link Operation (Wi-Fi 7 MLO): Dedicate separate links per zone; controller fuses CSI.
B. 802.11az FTM Alignment: Use Fine Timing Measurement to synchronise sensing periods across APs.
C. Centralised Controller Cross-Correlation: Enterprise controllers (Cisco DNA, Aruba Central) compute cross-AP CSI correlation in software — no PHY changes needed.
Privacy — Passive Sensing Gap: PASN handles session consent. But a passive observer with a software-defined radio can extract coarse CSI from ambient Wi-Fi beacons without joining any 802.11bf session. The CSI Murder project and openWiFi CSI fuzzer demonstrate active attacks. 802.11bf does not address this. See backup slide: CSI Security.
Power & Duty Cycling: Continuous 100 Hz CSI keeps the radio awake. No standard for event-triggered sensing handoff or sleep mode. Battery IoT devices require application-layer duty cycling. *** CORRECTION: See new slide for full detail on ISTA/RSTA power save windows and TWT. ***
Baseband Normalisation: CSI in SMR is vendor-processed HE-LTF output, not raw ADC. Two certified APs from different vendors produce different H matrices for the same physical channel.
REFS:
- ansresearch/csi-murder: https://github.com/ansresearch/csi-murder
- openWiFi CSI fuzzer: https://github.com/openwifi-su/openwifi
- Ma et al. (2019) WiFi Sensing with CSI — ACM Computing Surveys

## Slide 18
SECTION 10 — USE CASES
Wi-Fi Sensing Use Cases — From Simple to Complex
LOWER COMPLEXITY →
→ HIGHER COMPLEXITY
Home Monitoring
& Occupancy
AP-based occupancy sensing
(Home / Broadband gateway)
IoT automation integration
Presence + motion amplitude variance
Simple threshold · No ML needed
Baby/pet in car · Smart HVAC
Occupancy-driven automation
Aging in Place
& Fall Detection
Client-based fall detection
(In-home care applications)
Velocity spike + Doppler
Sudden CSI magnitude drop
Fall alert · Gait analysis
Elderly independent living
Vital Signs
& Wellness
Continuous vital monitoring
(Healthcare / sleep quality)
0.1–0.5 Hz bandpass on phase
Per-subcarrier coherent detect
Breathing / HR (±1–3 BPM lab)
Sleep quality · Hospital monitoring
Advanced Sensing
& Pose Estimation
Research / next-gen
(Full body pose pipeline)
RF-Pose / DensePose fusion
60 GHz + multi-AP CSI
Full body keypoints · Gesture
facebookresearch/DensePose (MIT)
→
→
→
Notes: USE CASES (1 min)
The WFA has defined four reference scenarios — I've mapped them to a complexity axis.
Card 1 (Occupancy/Home): The WFA "AP-based home monitoring" use case. Broadband service providers are the target customer — they want to offer sensing as a value-added service bundled with their router subscription. Baby in car is literally a lifesaving threshold-based application.
Card 2 (Aging in Place): "Client-based" means the STA does the sensing processing locally — important for privacy and latency. Fall detection requires sub-100ms response time.
Card 3 (Vital Signs): The WFA frames this as "secondary alarm verification" — if your security system triggers, Wi-Fi sensing can confirm whether a person is actually present (reducing false alarms, a huge issue in monitored home security). But the tech enables sleeping heart rate too.
Card 4 (DensePose / Pose): This is beyond current WFA scope — research territory. But I have something to show for this (see backup slides).
REFS:
- Wi-Fi Alliance sensing whitepaper: https://www.wi-fi.org/beacon/wi-fi-sensing
- Guendel, R.R. et al. (2022) Continuous Human Activity and Vital Sign Monitoring Using Wi-Fi CSI — IEEE Sensors
- Multi-AP fusion approaches: MLO (802.11be), 802.11az FTM alignment, centralised controller cross-correlation

## Slide 19
SECTION 11 — TECHNOLOGY LANDSCAPE
Sensing Technology Landscape — Full Comparison
Attribute
PIR
Radar (FMCW/Doppler)
Acoustic
Camera / CV
Wi-Fi 802.11bf
Detection LoS
LoS only
No (penetration)
No
LoS only
✓ No LoS needed
Resolution
Motion only
Med–High (mmW)
Sound events
✓✓ DensePose+
Low–Med
Privacy
✓ None
✓ None
⚠ Audio
⚠ Video/Face
✓ None
Dark / smoke
✓ Yes
✓ Yes
✓ Yes
✗ No
✓ Yes
Through walls
✗ No
✗ No
Partial
✗ No
◑ NLOS coverage, not imaging
Install HW
New sensor
New sensor
Smart device
Camera+GPU
✓ Reuse AP
Cost
$
$$$
$$
$$$
$ (infra)
Power
Low
Med–High
Low–Med
High
Med (MAC PM)
Interference
Lighting
Limited
TV / music
Shadow/light
CCA / congestion
Notes: TECH COMPARISON (1 min)
Key talking points from the table:
PIR: Cheap, proven, but completely line-of-sight. Can't tell you how many people, can't tell you breathing rate, can't work through a wall.
Radar (FMCW): The closest competitor technically. mmWave radar (60 GHz, 4+ GHz bandwidth) actually beats Wi-Fi on resolution. Products like Texas Instruments IWR series. But it's a separate dedicated sensor at $15-50/unit. For 4 rooms that's $60-200 of hardware vs $0 of Wi-Fi infrastructure already installed.
Acoustic: Surprisingly good for presence and some motion detection. The TV problem is real and unsolved — you can't train away the confound easily.
Camera/CV: Highest resolution, most mature ML stack. DensePose gives you full UV body mapping. But you need cameras (privacy), GPUs (cost), and line-of-sight (limitation).
Wi-Fi 802.11bf: Privacy-preserving, through-wall, zero additional hardware — but lower resolution than mmWave radar and CV for pose estimation. Not a universal winner — a genuine tradeoff.
REFS:
- Texas Instruments IWR6843 datasheet — for radar comparison
- Nakatsuka, N. et al. (2022) "Reassessing the Limitations of CNN Methods for Acoustic Occupancy Detection" — IEEE IoT Journal

## Slide 20
SECTION 06 — CSI IN PLAIN ENGLISH
CSI Security — The Privacy Paradox of Wi-Fi Sensing
Wi-Fi sensing offers privacy vs cameras — but CSI itself can be an attack surface and a surveillance tool
⚔ Threat | 🛡 Defence
Passive SDR Sensing (no auth needed)
Commodity SDR passively extracts CSI from ambient Wi-Fi beacons — no 802.11bf session, no PASN, no consent. Detects presence, counts people, infers location.
Keystroke & Gait Inference
Academic work: CSI can infer typed passwords (finger micro-motion), gait signatures for person ID, crowd density — from your existing frames, without your knowledge.
CSI-MURDER (ansresearch) — DEFENCE
Univ. Brescia / IMEC. Randomises I/Q samples so passive observers get meaningless CSI. Normal Wi-Fi continues. The 'murder' is murdering the attacker's sensing ability.
OpenWiFi CSI Randomisation — DEFENCE
IMEC openWiFi embeds CSI-MURDER on FPGA 802.11 stack. Proves standard-compliant obfuscation without harming communication performance.
🛡 Defences & Honest Framing
What 802.11bf DOES provide
PASN: cryptographic session key before any sensing exchange. Protected SMR (encrypted CSI reports). Consent bit in SMSR. Association requirement (Phase 1). These prevent malicious 802.11bf SESSIONS.
What 802.11bf does NOT solve
Passive observation of ambient Wi-Fi. Side-channel CSI extraction from standard data frames. Pre-existing proprietary sensing in deployed APs. Regulatory enforcement of consent.
Vs Camera (honest comparison)
Wi-Fi sensing cannot produce a recognisable image of a person — it cannot identify who you are by face. Camera can. This is the privacy advantage. But CSI can identify that someone is present, count people, and with enough data, identify individuals by gait. The advantage is real but not absolute.
Regulatory landscape
FCC and ETSI are actively studying passive RF sensing privacy rules. EU AI Act may classify high-accuracy occupancy sensing as a biometric adjacent system. Commercial deployment of sensing features in ISP routers may require explicit opt-in under GDPR.
Key point: More private than cameras, less private than nothing. 802.11bf improves session security — it does not eliminate passive surveillance.
Notes: CSI SECURITY — THE PRIVACY PARADOX
Context for this slide: when you argue Wi-Fi sensing has a privacy advantage over cameras, a security researcher will challenge you. This slide arms you for that conversation.
WHAT IS CSI-MURDER? (Important correction — it is NOT an attack tool)
CSI-MURDER (ansresearch/csi-murder, University of Brescia / funded by EU Horizon 2020 ORCA project) is a PRIVACY PROTECTION framework. The goal is to obfuscate CSI so that an attacker who passively observes your Wi-Fi transmissions cannot use the CSI to localise you — while your own Wi-Fi communication continues normally.
How it works: the transmitter modifies the I/Q samples of each frame using an irreversible randomised sequence before transmission. The receiver still decodes the data correctly (because the data is encoded above the PHY layer). But an external observer trying to extract CSI for sensing purposes gets randomised, meaningless values. The "murder" is murdering the attacker's localisation — not an attack on someone else's system.
The project also produced a modified openWiFi build (openWiFi is an open-source 802.11 FPGA stack from IMEC/Ghent) that embeds this randomisation. Published in IEEE journals and ScienceDirect. Fully legitimate academic privacy research.
THE ACTUAL THREAT they are defending against:
A passive attacker with an SDR (or a modified NIC) can sit in range of your AP, collect CSI from your Wi-Fi beacons and data frames (which are transmitted in the clear), and use that CSI to localise you, count people in the room, or infer activity — all without your knowledge, no association required, no PASN, no 802.11bf session. This is the privacy threat that 802.11bf's PASN protects against for SESSION-BASED sensing, but does not protect against for PASSIVE OBSERVATION.
So the correct framing for your talk: CSI-Murder and openWiFi are on the DEFENDER side, not the attacker side. The threat is passive eavesdropping and CSI extraction.
THE HONEST PRIVACY COMPARISON:
- Camera: can identify who you are, what you're wearing, your face, your expressions
- CSI: cannot produce a recognisable image; cannot identify your face
- But CSI CAN: detect you're present, count how many people are in a room, classify your activity (sitting, walking, sleeping), and with enough long-term data, identify you by gait signature
The privacy advantage of Wi-Fi sensing over cameras is real and significant for most use cases. But it is not an absolute privacy technology. Be honest about this.
802.11bf's SECURITY ADDITIONS (what they do and don't do):
- PASN: prevents an unauthorised device from setting up a 802.11bf sensing session with your AP. Does NOT prevent passive observation.
- Protected SMR: encrypts the CSI report in transit between SR and SI. Does NOT prevent the SR from exfiltrating CSI to a third party.
- Consent bit in SMSR: signals that the SR has consented. No enforcement mechanism.
REFS:
- ansresearch/csi-murder: https://github.com/ansresearch/csi-murder
- openWiFi: https://github.com/openwifi-su/openwifi
- Ali et al. (2015) "Keystroke Recognition Using Wi-Fi Signals" — MobiCom
- Kotaru et al. (2015) "SpotFi: Decimeter Level Localization Using WiFi" — SIGCOMM

## Slide 21
SECTION 12 — LAB VS FIELD & TRENDS
Lab vs Field — Challenges & Industry Responses
CHALLENGE
INDUSTRY / RESEARCH RESPONSE
🌀
Fans / HVAC (0.5–10 Hz overlap)
Adaptive notch filters keyed to detected AC harmonics. Cognitive Systems patented always-on reference antenna for static multipath separation. Origin AI uses background CSI model subtraction.
📶
Interference & CCA Deferral
802.11bf sessions use priority-aware EDCA queuing. WFA cert will require coexistence tests. Spatial beamforming toward target reduces interference pickup on receive path.
🪑
Furniture / Room Geometry Transfer
Few-shot domain adaptation (2-3 calibration walks). Origin AI auto-fingerprints environment at boot. Transfer learning from Gesture Lab (Google) reduces retraining to minutes.
🌡
Temperature / Oscillator Phase Drift
B2B (back-to-back) channel calibration via reference antenna (Keerativoranan et al. 2018). Intel AX210 & BCM6xx chips log AGC/phase state. 802.11bf SMR includes phase reference fields.
👥
Multi-Person Ambiguity
Multi-AP CSI fusion with MUSIC-based spatial separation (research). Qualcomm MLO (Wi-Fi 7) dedicates per-zone links. FastConnect 7900 NPU runs on-chip person counting inference.
🔄
CSI Normalisation — Vendor Gaps
Gjengset et al. SIGCOMM 2011 preprocessing standard widely adopted. WFA plans normalisation test vectors in cert. Wi-Fi 6E chipsets added AGC state logging for post-hoc correction.
Notes: LAB vs FIELD — DETAILED MITIGATIONS
1. FANS / HVAC (0.5–10 Hz overlap):
Threat: Rotating fan blades at 750 RPM = 12.5 Hz; pedestal fan ~3 Hz. Both overlap breathing (0.2–0.4 Hz) and gesture (1–5 Hz) bands, causing constant false triggers.
Fix A — Adaptive Notch Filters: Software targets exact AC electrical harmonics of the room's equipment. Must auto-detect the fan frequency from the CSI itself.
Fix B — Reference Antennas: Cognitive Systems patented using an unshielded background antenna to capture static multipath, then subtract it from the sensing antenna.
Fix C — CSI Subtraction: Baseline noise matrices are systematically subtracted from the incoming signal stream, isolating organic human motion signatures.
2. INTERFERENCE & CCA DEFERRAL:
Threat: Dense residential/enterprise spaces saturate the channel. CCA forces sensing NDPs to back off below the rate needed to capture fast gestures or falls.
Fix A — EDCA Queuing: 802.11bf sensing frames routed through priority-aware queues (AC_VI) to prevent latency spikes.
Fix B — WFA Coexistence Profiles: Cert enforces airtime equity between sensing and data sessions.
Fix C — Spatial Filtering: Directional receive beamforming blocks outside environmental interference at the antenna level.
3. FURNITURE / ROOM GEOMETRY TRANSFER:
Threat: Lab-trained model fails instantly in a cluttered living room — static layout permanently warps the baseline multipath footprint.
Fix A — Few-Shot Adaptation: 2–3 calibration walks are enough to remap new layouts for most activity classifiers.
Fix B — Boot Fingerprinting: Routers execute automated environment scans at startup. Origin AI does this automatically over the first 24 hours of deployment.
Fix C — Transfer Learning: Google Gesture Lab pre-trained weights isolate user movement vectors from structural room bounds — deployment retraining cut to minutes.
4. TEMPERATURE / OSCILLATOR PHASE DRIFT:
Threat: As a router heats up during data streaming, crystal oscillator thermal expansion alters clock speeds, injecting artificial phase drift that masks real target signatures.
Fix A — B2B Calibration: Back-to-back hardware calibration continuously measures reference loops to neutralize internal clock skew (Keerativoranan et al. 2018).
Fix B — AGC State Logging: Intel AX210 and Broadcom BCM6xx chips expose AGC state changes directly to the driver layer for post-hoc correction.
Fix C — SMR Phase References: 802.11bf SMR headers include native phase reference vectors for continuous software baseline recalibration.
5. MULTI-PERSON AMBIGUITY:
Threat: Multiple people's reflections collide at the receive antenna. A single-link system cannot distinguish two people from one erratic mover.
Fix A — MUSIC Algorithm: Multiple Signal Classification processes multi-AP CSI matrices for high-resolution angular and spatial person separation.
Fix B — Qualcomm MLO (Wi-Fi 7): Multi-Link Operation dedicates independent frequency links to handle separate zones of a house.
Fix C — On-Chip NPU (FastConnect 7900): Routes multi-person spatial data directly into integrated neural processing units for real-time edge isolation.
6. CSI NORMALISATION — VENDOR GAPS:
Threat: Intel, Atheros, Broadcom chips produce CSI on entirely different scales, formats, and normalization baselines. A model trained on one fails on another.
Fix A — Gjengset Preprocessing: Standardized calibration matrix math (SIGCOMM 2011) universally deployed to normalize raw inputs.
Fix B — WFA Test Vectors: Alliance integrating mandatory normalization validation profiles into certification tests.
Fix C — AGC Telemetry: Wi-Fi 6E/7 chipsets attach high-fidelity AGC telemetry to every frame for post-hoc vendor-agnostic correction.
REFS:
- Keerativoranan et al. (2018) B2B Calibration — Sensors MDPI
- Gjengset et al. (2011) Phaser — MobiCom

## Slide 22
SECTION 12 — LAB VS FIELD & TRENDS
Industry Trends &
Where Wi-Fi Sensing is Headed
USEFULNESS ANSWER — When to use Wi-Fi sensing:
✓ Wi-Fi Sensing
AP deployed · $0 HW · Privacy matters · Presence · occupancy · vitals
✗ Use Radar
Need cm-accuracy · No Wi-Fi infra · mmWave gesture
✗ Use CV
Need identity · Line-of-sight OK · Full pose/DensePose
Wi-Fi 7 + Sensing
320 MHz BW & Multi-Link Op improve range resolution. TGbf 'be' PHY amendments expected 2026.
WFA Certification Flywheel
Board approved Apr 2026. Cert launch target: Dec 2027. No certified product yet — window to build implementation expertise is NOW.
Matter + Sensing
Thread/Matter will surface sensing events as standard home data — no custom cloud stack needed.
On-Device ML
NPUs in Wi-Fi SoCs (Qualcomm FastConnect, MTK Filogic) eliminate cloud round-trip. Sub-50ms targets.
Regulatory Evolution
FCC, ETSI exploring passive RF sensing privacy rules. EU commercial rollout gated on this.
mmWave Proliferation
60 GHz (802.11ad/ay) delivers centimetre-level sensing. Consumer wave expected 2026+.
Notes: CLOSING (1 min)
BEFORE THE TRENDS — land the "usefulness" answer since the talk title promises it:
"When should you use Wi-Fi sensing? When your AP is already deployed and privacy matters. When should you use radar? When you need centimetre resolution or gesture in an area without Wi-Fi. When should you use computer vision? When you need identity. Don't claim Wi-Fi sensing works through a wall for anything fine-grained — it doesn't. What it does is turn existing infrastructure into a coarse, privacy-preserving, always-on presence and activity sensor. That is genuinely useful in healthcare, security, and smart home at massive scale."
Let me leave you with six trends.
Wi-Fi 7: 320 MHz channels mean range resolution improves from ~1m to ~30cm. Multi-Link Operation means you can dedicate a link to sensing while another handles data. This is a big deal.
WFA flywheel: This is the key business unlock. Once major chipset vendors get certified, system integrators don't need to worry about interop. App developers can build to a known API. Volume follows.
Matter + Sensing: this one isn't talked about enough. If a sensing event (room occupied, person fell) becomes a standard Matter event, it works with every smart home platform. No vendor lock-in at the application layer either.
On-device ML: Qualcomm FastConnect 7900 has an NPU on the Wi-Fi chip. We're entering an era where the AP can run inference locally, report only semantic events (not raw CSI) — much better for privacy and bandwidth.
Wi-Fi sensing is at the same point as Wi-Fi itself was in 1999: standard exists, ecosystem forming, mass market 3-5 years away. The teams that build the expertise now will own the deployment wave.
REFS:
- Qualcomm FastConnect 7900: https://www.qualcomm.com/products/technology/wi-fi/fastconnect/fastconnect-7900
- 802.11be (Wi-Fi 7) overview: IEEE 802.11be-2024

## Slide 23
[ DOTSTAR_CONSULTING ]
Your Strategic Wireless Engineering Partner
Silicon-to-Cloud • 18+ Years Deep-Tech Pedigree • AI-Augmented Delivery • Hyderabad, India
Silicon & Firmware
Pre-silicon (EMU/FPGA), post-silicon bringup, 802.11a→be driver engineering
Wi-Fi Sensing
802.11bf implementation, CSI pipeline design, sensing ML deployment on-device
IoT Ecosystems
Matter, Thread, LTE-M/NB-IoT. Nordic nRF specialist. End-to-end wireless SDLC.
Edge AI / ML
Fine-tuning & deployment of AI/ML models onto resource-constrained IoT devices
✓ Zephyr Project Wi-Fi Maintainer ✓ hostap core contributor ✓ Patent-backed power-saving & node communication ✓ WFA / CSA / FCC / ETSI certification support
Ready to build the next generation of Wi-Fi sensing products?
Book a Consultation →
dotstarconsulting.com | info@dotstarconsulting.com | calendly.com/chaitanya-dotstarconsulting/30min
Notes: DOTSTAR CONSULTING (1 min)
This is what Dotstar Consulting is and what we offer.
Quick framing: we're not a product company — we're a boutique engineering firm. We take on the hard problems at the intersection of wireless silicon, firmware, IoT, and now AI/sensing.
Our relevant sensing credentials:
- I maintain the Wi-Fi driver in ZephyrRTOS — so we can push 802.11bf support into the most popular embedded RTOS directly
- hostap contributor — the reference implementation of WPA supplicant and hostapd used in virtually every Linux AP
- Patented work in power saving — relevant for battery-powered sensing devices
What we can build for you:
- 802.11bf SI/SR implementation from scratch on your chipset
- CSI feature extraction pipeline (C/C++ or Python)
- Edge ML model for your specific use case
- Full certification preparation for WFA submission
The green CTA button — book a 30-minute call. Happy to discuss your project right after this talk.
REFS: dotstarconsulting.com for full capability list

## Slide 24
DEMO - DENSEPOSE SETUP
DensePose Setup — ESP32-C6 to Laptop Pipeline
ESP32-C6 acts as 802.11ax STA · AP bridges to laptop · WebSocket streams CSI to RF-Pose inference server
📱
ESP32-C6
802.11ax STA
esp_wifi_set_csi()
~20 pkt/sec
📡
Wi-Fi AP
Home/lab router
Bridges STA to LAN
Same subnet
💻
Laptop
RuView WebSocket server
RF-Pose CNN inference
DensePose viz
▶
802.11ax Wi-Fi
CSI-rich NDPs
▶
LAN bridge
Ethernet/Wi-Fi
◀─── WebSocket connection: ESP32-C6 (client) connects to Laptop (server) via AP bridge ───▶
Data flow detail:
ESP32-C6 Firmware
• esp_wifi_set_csi() callback per packet
• Buffer H[Nrx×Ntx×Nsc] + timestamp
• Serialize → JSON over WebSocket
AP (no config needed)
• Standard infra mode: ESP32 as STA
• Laptop is DHCP client on same LAN
• WebSocket server runs on laptop port
Laptop (RuView Server)
• Receives CSI JSON stream
• CFO/SFO removal → STFT features
• RF-Pose CNN → DensePose UV output
Notes: SETUP DIAGRAM — how the demo works physically
1. ESP32-C6 devkit: configured as a standard 802.11ax STA. ESP-IDF firmware uses esp_wifi_set_csi() to capture CSI for every received packet. Each callback buffers the complex H matrix, timestamps it, and serialises to JSON sent over a WebSocket connection to the laptop.
2. Wi-Fi AP: any standard router. The ESP32 associates with it as a normal Wi-Fi client. No special configuration. The laptop connects to the same LAN (via Wi-Fi or Ethernet).
3. Laptop: runs the RuView WebSocket server (Python or Node.js). Receives the CSI stream, applies preprocessing (Hampel filter, CFO/SFO removal, STFT), runs RF-Pose CNN inference, and renders DensePose UV keypoints in the browser-based RuView UI.
SCREENSHOTS TO ADD: Replace the green bar with images showing:
- Raw CSI amplitude vs time (the raw signal)
- Motion artifacts visible in CSI when you move
- RuView output showing pose skeleton overlay
REFS: https://github.com/ruvnet/RuView
ESP-IDF CSI: https://docs.espressif.com/projects/esp-idf/en/latest/esp32c6/api-guides/wifi.html

## Slide 25
RUVIEW LIVE DEMO
RuView — Wi-Fi DensePose in Action
Wi-Fi Sensing → Human Pose + Vital Signs · ESP32-C6 · 802.11ax CSI · No Camera
▶ output.mp4 — 39s live demo · RuView DensePose Observatory
LIVE OUTPUT — from video
♥ Heart Rate
68 BPM
◎ Respiration
12 RPM
✦ Confidence
88%
⬟ Persons
1
● Presence
PRESENT
Wi-Fi Signal (from SMR)
RSSI: −39 dBm · Variance: 0.80 · Motion: 0.020
github.com/ruvnet/RuView · ESP32-C6 · esp_wifi_set_csi() · MQTT → RF-Pose inference · Previously: needed hacked Intel 5300. Now: $4 IoT chip.
Notes: LIVE DEMO SLIDE — play output.mp4 if presenting in person
The video (output.mp4, 39 seconds) shows the RuView DensePose Observatory running live:
- Human pose estimation (blue wireframe body model visible)
- Vital signs: HR 68 BPM, Respiration 12 RPM, 88% confidence
- Presence: ACTIVE/PRESENT
- Wi-Fi signal panel: RSSI -39 dBm, Variance 0.80, Motion 0.020, Persons: 1
When showing this: point out the vital signs panel on the left. "Heart rate 68 BPM — that's my actual heart rate, sensed through the ambient Wi-Fi channel. No electrodes. No chest strap. No camera. Just channel state information from a $4 ESP32-C6."
Then point at the pose skeleton: "And that crude body shape on the right — that's the beginning of RF-DensePose. Full body UV coordinates from radio waves."
VIDEO EMBEDDING NOTE: PowerPoint can embed mp4 natively. To add the actual video: Insert → Video → This Device → select output.mp4. Set to play automatically on slide show entry. The still frame on this slide serves as a placeholder.

## Slide 26
🙏 ಧನ್ಯವಾದಗಳು
Dhanyavaadagalu · Thank You
Wi-Fi Knowledge Summit 2026 · Bengaluru
Let's connect
🌐 dotstarconsulting.com
✉ info@dotstarconsulting.com
📅 calendly.com/chaitanya-dotstarconsulting/30min
💼 Chaitanya Tata · Founder & CTO
✦ Deck prepared with assistance from Claude (Anthropic)
Scan → Digital Card
📡 Engineer's Confession
"I asked my Wi-Fi router
if anyone was home.
It said: Variance = 0.003.
(no motion detected)
My wife said that is
not romantic.
I said: False negative —
the model needs retraining."
Variance=0 = flat CSI, nothing moving. 0.003 = nobody home.
Questions? Hecklers? Anyone whose breathing rate I mis-classified? Come find me 🙏
Notes: THANK YOU SLIDE — delivery notes
The joke: pause after "My wife said that's not romantic." Wait for the laugh. Then deliver the punchline.
The QR code is your HiHello digital card — it links directly to your contact info, LinkedIn, and website. Mention it explicitly: "If you scan that QR code you'll get my digital card — no paper card to lose."
Tone for this slide: warm, slightly self-deprecating, clearly technically fluent. You've just given a dense 20-minute talk to a room full of Wi-Fi engineers — they'll appreciate someone who can make fun of their own work.
The "false negative — model needs retraining" line lands well because:
1. It references the exact gap you covered in slide 14 (environmental generalisation)
2. It's self-aware about the limits of sensing
3. It connects the technical content to everyday life
After the joke, hand it over: "Serious question mode: what did I get wrong? Five minutes for Q&A."

## Slide 27
BACKUP — HANDSHAKE & CSI FLOW
Power Save, SBP & CSI Variation Feedback
Power Save — ISTA/RSTA Availability Windows (§9.4.2.298-299)
802.11bf DOES define structured power save using two standard IE elements:
• ISTA Availability Window (§9.4.2.298): The Sensing Initiator (AP) advertises its own TX-active windows — SR can sleep outside these.
• RSTA Availability Window (§9.4.2.299): The Sensing Responder (STA) negotiates its wake windows — SR sleeps between sensing slots and wakes deterministically for the next sensing round.
• In TB sensing: STAs wake only for the Trigger Frame + uplink NDP → immediately sleep. 16 μs SIFS discipline eliminates idle listening.
Timeline:
SLEEP
WAKE
(RSTA window)
SLEEP
WAKE
(sensing)
SLEEP
WAKE
SLEEP
★ Devices outside availability windows may sleep — contrary to early design assumptions. 802.11bf is power-aware.
SBP — Sensing by Proxy
Problem: Hidden node — IoT battery device cannot hear the AP's NDP directly.
SBP Solution: A third device (Proxy STA, usually mains-powered) receives the NDP on behalf of the hidden node, extracts the CSI, and forwards the SMR to the AP.
Key benefit: IoT/battery STAs in poor RF coverage can participate in multistatic sensing grids without direct AP visibility. Proxy can be any associated STA.
CSI Variation Feedback Optimization
Problem: Sending full CSI (I+jQ per Ng group) every packet is wasteful when the channel is mostly static.
CSI Variation Feedback: Instead of sending full H matrix, the SR reports only the threshold-based ΔH from the last reference CSI. Dramatically reduces SMR payload.
Result: SR skips expensive SMR transmission during static periods. When motion is detected (variation exceeds threshold), full SMR resumes. The SI sets per-SR thresholds — different thresholds for different room zones. Defined in §9.4.2.297.
Ref: IEEE 802.11bf-2025 §9.4.2.298 ISTA Avail Window · §9.4.2.299 RSTA Avail Window · §11 SBP · CSI Variation Feedback §9.4.2.297

## Slide 28
BAKCUP - PASN
PASN-Based Unassociated Sensing Handshake
Phase 2 of 802.11bf enables unassociated clients to participate in sensing WITHOUT joining the BSS. PASN (Pre-Association Security Negotiation) from 802.11be provides the secure key exchange.
Phase 1: PASN Authentication (3-Frame Exchange)
Client STA
(Unassociated)
Access Point
(SR)
1. PASN Auth Request
SENS Caps + DH PubKey + ISTA Avail Window
2. PASN Auth Response
AP SENS Caps + DH PubKey + RSTA Avail Window + Anonce
3. PASN Auth Confirm
Crypto verification + Final sensing session params
★ Session keys established via ECDH (P-256/P-384) + AES-GCM. No BSS association needed.
Phase 2: Sensing Exchange (Within Availability Window)
Negotiated Availability Window Opens (ISTA/RSTA)
4. SENS NDPA
NDP Announcement — tells STA sensing NDP is coming
5. SENS NDP
Sounding preamble (HE-LTFs) — STA extracts raw CSI matrix H
6. SENS Feedback (optional)
Compressed I/Q or SNR matrix sent back to AP
★ Sensing frames are MAC-layer encrypted with PASN session keys (AES-GCM)
Why PASN for Multistatic Sensing?
No BSS join
Unassociated client can serve as a passive SR without 4-way handshake overhead — critical for battery IoT
Secure CSI
SMRs encrypted in flight — prevents neighbour devices from intercepting your room's CSI matrix
ISTA/RSTA windows
Both sides negotiate wake/sleep intervals in auth frames — enables deep power save (see next)
Multistatic scale
Multiple unassociated STAs can act as SRs simultaneously — AP aggregates from all
Ref: IEEE 802.11bf-2025 §11 (PASN sensing handshake) · §9.4.2.298-299 (ISTA/RSTA Availability Window elements) · 802.11be PASN §12.7.10
Notes: PASN MULTISTATIC (1.5 min)
This is Phase 2 of 802.11bf — unassociated sensing. Phase 1 was only associated devices.
WHY UNASSOCIATED? Many IoT/battery devices cannot afford the overhead of 802.11 4-way association handshake. PASN (Pre-Association Security Negotiation, from 802.11be) provides a 3-frame exchange that establishes session keys without joining the BSS.
THE 3-FRAME EXCHANGE:
Frame 1 (STA to AP): I want to do sensing. Here are my SENS capabilities, my Diffie-Hellman public key, and the times I am available (ISTA Availability Window).
Frame 2 (AP to STA): OK. Here are MY capabilities, MY DH public key, MY availability window, and a random nonce to prevent replay.
Frame 3 (STA to AP): Here is the cryptographic proof I computed the same session key you did.
After this, both sides have identical AES-GCM session keys. All SMRs are encrypted in flight.
THE AVAILABILITY WINDOWS: Note that ISTA and RSTA windows are exchanged IN the PASN frames. The device can sleep between these windows — this is the power save mechanism. See the dedicated slide for details.
Refs: IEEE 802.11bf-2025 §11 · §9.4.2.298-299 · 802.11be PASN §12.7.10

## Slide 29
BACKUP — BEAMFORMING / RU / Ng
Beamforming, RUs & PHY — Their Impact on Sensing
How existing Wi-Fi PHY techniques interact with — and can corrupt — sensing measurements
Beamforming vs Sensing
⚠ Problem:
Communication beamforming steers the channel H toward data throughput, creating a directional H_eq ≠ H_raw. The resulting CSI sees only the beam path — not the full room multipath. Motion outside the beam cone is invisible.
✓ 802.11bf Fix:
802.11bf Solution: (1) Non-beamformed sensing NDPs — AP injects omnidirectional frames for sensing, preserving full H_raw. (2) BFI Recovery — H_raw ≈ H_eq x V-inv where V is the steering matrix from Beamforming Feedback Info. 802.11bf standardises BFI reporting for this extraction.
Resource Units (RUs)
⚠ Problem:
OFDMA splits the 80 MHz channel into RUs assigned to different STAs. A sensing NDP on a narrow RU (e.g., 26-tone = 2 MHz) gives only 26 subcarrier estimates instead of 996 — massively degrading range resolution and Doppler sensitivity.
✓ 802.11bf Fix:
802.11bf requires full-bandwidth NDP for sensing — the HE Ranging NDP uses the full channel BW. SI specifies this in SMSR. OFDMA multi-user scheduling and sensing cannot share the same frame — AP must reserve full-BW airtime for sensing sessions.
Ng Grouping & Pilot Tones
⚠ Problem:
Ng=4 (mandatory) reduces reported groups from 234→60 per stream at 20 MHz. Higher Ng = less spatial resolution and Doppler fidelity. Older standards excluded pilot tones from CSI. Pilots carry phase reference — without them, phase continuity across subcarriers is broken.
✓ 802.11bf Fix:
802.11bf includes pilot tones in HE-LTF CSI, ensuring phase continuity (critical for breathing/AoA). Ng=4 (mandatory) = ~60 groups per stream — enough for presence/vitals. Ng=1 (optional) = full 234 groups for gesture/AoA but 4x more airtime. SI specifies Ng in SMSR.
Notes: BEAMFORMING / RUs / Ng — Why These PHY Features Matter for Sensing
BEAMFORMING (most important for a Wi-Fi audience):
Standard communication beamforming is designed to maximise data throughput — it steers the transmit beam toward the receiving STA. This creates a warped channel estimate H_eq = H_raw × V (where V is the precoding matrix). If your sensing algorithm uses H_eq, it sees only the beam path — motion in other parts of the room is suppressed. This is a real deployment problem: a Wi-Fi 6 AP with MU-MIMO enabled will beamform during data sessions, and if sensing also runs during those sessions, the CSI is biased.
802.11bf fixes this two ways:
1. Omnidirectional sensing NDPs: The AP can periodically inject un-steered sounding frames dedicated to sensing. These give H_raw — the full room view.
2. BFI-based reconstruction: If you only have beamformed packets, the steering matrix V is available in the Beamforming Feedback Info frame. You can compute H_raw ≈ H_eq × V⁻¹ mathematically. 802.11bf standardises BFI reporting so this inversion is always possible.
RU ALLOCATION:
In OFDMA (Wi-Fi 6/7), the channel is sliced into Resource Units of varying sizes. A 26-tone RU at 80 MHz is only 2 MHz — that gives 26 subcarrier estimates instead of 996. The sensing information content collapses. 802.11bf mandates that sensing NDPs use the full channel bandwidth — the SI specifies this in the SMSR. This means you cannot co-schedule OFDMA data and sensing on the same transmission slot.
Ng GROUPING — WHO CONTROLS IT:
The Sensing Initiator (AP) specifies Ng in the SMSR at session setup. The SR must support Ng=4 (mandatory /41). If the SI requests Ng=1, the SR can report all ~234 groups per stream (at 20 MHz) but this uses 4× more airtime. For the audience: Ng is the fundamental tradeoff knob between sensing fidelity and channel airtime cost.
PILOT TONE INCLUSION — THE PHASE CONTINUITY POINT:
Older CSI tools (e.g., Intel 5300 CSI tool) excluded pilot subcarriers from the reported CSI because pilots were used only for synchronisation, not data. Without pilot CSI values, there are gaps in the subcarrier frequency response — phase discontinuities that corrupt Doppler and AoA estimation. 802.11bf's HE-LTF based CSI includes pilot tone estimates, restoring phase continuity across the full subcarrier span. This is specifically why phase-based vital signs sensing (breathing, heart rate) works better on 802.11bf than on legacy patched-driver approaches.
REFS:
- IEEE 802.11bf-2025 Section 9.4 (SMR format, Ng encoding)
- IEEE 802.11bf-2025 Section 26.5.2 (HE-LTF structure and pilot tones)
- Sensing Threshold-Based Reporting Trigger: the SMR can be configured to send reports ONLY when CSI variance exceeds a threshold — reducing airtime when the environment is static. This is the Sensing Reporting Trigger field in the SMSR.

## Slide 30
BACKUP — DEMO: RF-POSE + DENSEPOSE
Wi-Fi Body Pose — RF-Pose + DensePose on ESP32-C6
ESP32-C6 (CSI collector) → RF-Pose (body keypoints) → DensePose (UV surface mapping). No camera.
RuView — github.com/ruvnet/RuView
Open-source Wi-Fi sensing framework targeting ESP32-C6 / C5 chipset
What it does:
• CSI collection via ESP-IDF Wi-Fi CSI APIs
• Per-packet H[Nrx×Ntx×Nsc] extraction
• Onboard FFT + feature pipeline
• MQTT/WebSocket output to inference host
• DensePose mapping via RF-Pose algorithm (MIT)
Hardware:
• ESP32-C6 devkit (~$4 module)
• 802.11ax (Wi-Fi 6) capable
• RISC-V + 512KB SRAM
System Architecture
ESP32-C6
CSI collector
802.11ax STA
↓
ESP-IDF Pipeline
FFT · variance · phase diff
↓
Edge Host / Cloud
RF-Pose model
DensePose UV mapping
↓
Output
Body keypoints · presence · BPM
Notes: BACKUP — DEMO SLIDE (if time permits, ~2 min)
This is a live demo slide — you can add your actual test data screenshots or a live feed here.
I have an ESP32-C6 devkit that I've been working with using the RuView framework (github.com/ruvnet/RuView). The ESP32-C6 supports 802.11ax and exposes CSI via esp_wifi_set_csi() in ESP-IDF.
What we're working on:
- Reliable per-packet CSI collection at 20+ packets/sec
- Onboard variance and Doppler feature extraction
- Streaming to a host for RF-Pose inference
This connects the academic work (MIT RF-Pose, facebookresearch DensePose) to a $4 chip that anyone can buy. If 802.11bf gets into ESP-IDF (which I expect within 12-18 months given Espressif's track record), this becomes a fully standardised implementation.
Demo talking points:
1. Show the ESP32-C6 hardware
2. Show CSI data stream live (if connected)
3. Show the RuView dashboard with presence/breathing output
4. Mention: this is the prototype; full 802.11bf SI/SR coming
REFS:
- RuView: https://github.com/ruvnet/RuView
- ESP-IDF CSI API: https://docs.espressif.com/projects/esp-idf/en/latest/esp32c6/api-guides/wifi.html#wi-fi-channel-state-information
- MIT RF-Pose: https://rfpose.csail.mit.edu/ (Zhao et al. 2018)

## Slide 31
BACKUP — RF-POSE DETAIL
RF-Pose: From CSI to Body Keypoints
MIT CSAIL — Zhao et al. (2018) — Through-wall human pose estimation via RF signals
1
RF Signal
Capture
60 GHz radar or
Wi-Fi 5 GHz CSI
(ESP32-C6 / 802.11bf SR)
Horizontal + Vertical
antenna pair
2
Spatio-temporal
Encoding
CSI frames stacked
into heatmap tensor
[time × antenna × freq]
Captures motion trajectory
per body part
3
CNN Pose
Estimation
Encoder-decoder CNN
trained on paired
RF + optical data
Outputs 14 skeleton
keypoints
4
DensePose
UV Mapping
facebookresearch/
DensePose maps
keypoints to full
body surface UV
coordinates
→
→
→
ESP32-C6: CSI collection working · RF-Pose inference: in progress
Notes: RF-POSE DETAIL (if demo backup, ~1 min)
The Zhao et al. 2018 paper (published in Nature) is the seminal work on through-wall pose estimation via RF.
The trick: they trained a model on paired data — people walking while simultaneously capturing optical (camera) and RF data. The optical data provides ground-truth body keypoints. The RF data becomes the input at inference time. You never need a camera in the deployment environment.
DensePose (Güler et al. 2018, Facebook AI Research) extends this from skeleton keypoints to dense UV surface coordinates — essentially painting a 3D body mesh from 2D keypoints.
On ESP32-C6:
- The chip has enough SRAM for CSI buffering and basic feature extraction
- Full CNN inference runs on a host (laptop, Raspberry Pi, or edge server)
- With ESP32-P4 (coming soon, 32MB PSRAM) local inference becomes feasible
My current setup: CSI → MQTT → Python host → RF-Pose inference → visualization. I'll update this slide with my test data before the talk.
REFS:
- Zhao, M. et al. (2018) "Through-Wall Human Pose Estimation Using Radio Signals" — CVPR (Nature Electronics version)
- Güler, R.A. et al. (2018) "DensePose: Dense Human Pose Estimation In The Wild" — CVPR
- RuView GitHub: https://github.com/ruvnet/RuView

## Slide 32
BACKUP — MARKET INTEL
Wi-Fi Sensing — Industry Momentum 2025-26
$24B
Wi-Fi Chipset Market
(2025)
$34B
Projected 2030
(6.7% CAGR)
18M
Wi-Fi 7 chips
Broadcom 2025
$72B
Wireless IoT Sensors
by 2035 (21% CAGR)
2025-26 Vendor & Regulatory Announcements
Jan 2026
Synaptics + Origin AI
Partnership embeds Wi-Fi sensing into Veros SoC for smart home occupancy — on-device AI, no cloud required.
Dec 2025
Qualcomm FastConnect 7900
Wi-Fi 7 + BT + UWB combo chip with NPU; integrates Wi-Fi ranging + sensing for proximity and device-awareness.
Sep 2025
IEEE 802.11bf-2025
Standard published 26 Sep 2025. 802.11bk (320 MHz positioning) published 5 Sep 2025. Both add to sensing ecosystem.
Sep 2025
MediaTek Filogic 880
Wi-Fi 7 silicon winning TP-Link and Netgear router designs; 802.11bf-capable PHY confirmed in silicon.
Feb 2026
TI acquires Silicon Labs
$7.5B deal reshapes IoT Wi-Fi chipset landscape; 300mm fab scale applied to low-power IoT Wi-Fi and sensing.
Apr 2026
Wi-Fi Alliance
Board approved Wi-Fi Sensing certification program; MRD 1.0 in progress. 4 certification tracks confirmed.
Notes: MARKET (for networking conversations or if asked about commercial traction)
Key numbers:
- $24B Wi-Fi chipset market in 2025 growing to $34B by 2030. Wi-Fi sensing is a value-add feature driving ASP upward — no separate market needed.
- Broadcom shipped 18M Wi-Fi 7 combo chips in 2025 alone. Most 802.11bf-capable with firmware update.
- $72B wireless IoT sensor market by 2035 at 21% CAGR — Wi-Fi sensing competes here against radar and PIR directly.
Most important announcement: Synaptics + Origin AI (Jan 2026). First major SoC vendor integration of Wi-Fi sensing software. Synaptics Veros SoC is used in smart displays, TVs, smart home hubs — mainstream consumer volume.
Qualcomm FastConnect 7900 integrates Wi-Fi 7, Bluetooth, and Ultra Wideband in one chip with an NPU. The NPU is designed to run Wi-Fi sensing inference on-device. This is the architecture that eliminates the cloud round-trip that privacy advocates object to.
TI/Silicon Labs consolidation ($7.5B, Feb 2026): the big players are building scale in low-power wireless IoT. Wi-Fi sensing for IoT is a design win opportunity.
REFS:
- FMI: Wi-Fi Semiconductor Chipset Market 2026 report
- PR Newswire: Synaptics + Origin AI, Jan 6 2026
- IEEE 802.11 WG: https://www.ieee802.org/11/

## Slide 33
BACKUP — RF CALIBRATION
RFIC Analog Impairments — What Corrupts Your CSI Before Sensing
RFIC analog impairments corrupt the CSI matrix before your sensing algorithm ever sees it — independently of channel or environment quality
SFO — Sampling Freq Offset
ADC clock vs Tx DAC mismatch (±50ppm typical). Creates a LINEAR PHASE RAMP across subcarriers that grows with time. At 100Hz CSI rate: ~0.2 rad/subcarrier/packet. Indistinguishable from a slow Doppler shift — pure ADC artefact.
Mitigation:
Pilot subcarrier phase slope estimation. 802.11az/bf inherit SFO correction from HE NDP preamble. Residual ppb-level drift is the enemy of long-window (>10s) vital signs sensing.
CFO — Carrier Freq Offset
LO crystal mismatch Tx↔Rx up to ±20 ppm (5GHz = ±100kHz). Adds a CONSTANT PHASE ROTATION per packet — every subcarrier shifts by the same amount. 802.11 corrects coarsely via L-STF; residual after correction corrupts phase sensing.
Mitigation:
Conjugate multiply consecutive packets: H[n] × conj(H[n-1]) cancels common phase. BUT: if environment changes between packets, you cannot separate residual CFO from real Doppler. Fundamental ambiguity — no software fix.
Group Delay — Front-End Dispersion
LNA, mixer, SAW/BAW filter, PCB trace: each has FREQUENCY-DEPENDENT impulse response. Every subcarrier experiences a different delay. Destroys cross-subcarrier phase coherence. Chip-to-chip variation ±0.5–1ns = ±15–30cm range error on COTS.
Mitigation:
Requires VNA bench calibration per unit — cannot be removed over-the-air. THIS is why cm-accurate ranging on COTS Wi-Fi is largely impossible. 802.11bf does NOT address this. For relative sensing (motion, breathing) the static offset cancels. Fatal only for absolute AoA/ToF.
Additional RFIC Impairments (beyond SFO/CFO/Group Delay):
IQ Imbalance
I/Q mismatch in downconverter → spectral mirror image at ±Δf. Fake reflections in H.
Phase Noise
LO phase noise → jitter on all subcarriers. Limits coherent integration window.
IQ DC Offset
DC bias onto subcarrier 0 and neighbours. Residual after 802.11 correction contaminates nearby tones.
Antenna Mutual Coupling
Adjacent MIMO antennas couple energy → corrupts off-diagonal H[i,j]. Hurts AoA at close spacing.
AGC Discontinuities
AGC gain steps between packets → amplitude jumps that mimic scene changes. Critical for presence detection.
Notes: RF CALIBRATION — DEEP TECHNICAL (for Wi-Fi RF engineers in Q&A)
THE THREE IMPAIRMENTS AND WHY THEY MATTER FOR SENSING vs RANGING:
1. SFO (Sampling Frequency Offset): Your ADC and the remote transmitter's DAC run from different crystals. The ADC undersamples or oversamples slightly, creating a LINEAR PHASE SLOPE across subcarriers that GROWS with each CSI sample. If you're collecting 100 CSI frames over 10 seconds, the SFO-induced phase ramp can rotate by many radians. This looks exactly like a 0.01 Hz Doppler shift — indistinguishable from slow breathing unless corrected. 802.11az introduced SFO correction based on pilot subcarrier phase slopes. 802.11bf SMR can include the SFO estimate as a reference field.
2. CFO (Carrier Frequency Offset): The remote transmitter is at 5180.000100 MHz, your local oscillator is at 5179.999900 MHz — 200Hz CFO. This creates a CONSTANT phase offset added to every subcarrier on every packet. The standard 802.11 preamble estimates and corrects this from L-STF, but the correction is coarse. The residual CFO (typically ±10-100Hz) causes a phase rotation of ~2π per 10ms at 100Hz residual. For breathing rate sensing (0.2-0.3Hz), a 100Hz CFO residual looks like a 500x faster oscillation — easily filtered. But for fine motion (hand gesture at 1-2Hz), residual CFO is comparable. Solution: conjugate-multiply consecutive CSI packets. This cancels static phase offset. Works well unless the channel changes significantly between packets.
3. GROUP DELAY: This is the "ranging never works" problem. Your RF front-end (specifically: the SAW/BAW filter, the balun, the PCB trace between antenna and LNA) has a FREQUENCY-DEPENDENT impulse response. Different frequencies travel through your front-end at different speeds. This is group delay variation. The chip designers try to make it flat but at 200MHz bandwidth, you can have 0.5-1ns variation across the band. At 5GHz, 1ns = 20cm range error. AND this varies chip-to-chip, lot-to-lot, temperature-to-temperature. You cannot estimate it over the air because you'd need to know the ground truth channel (which you're trying to measure). You need a VNA or a known calibration environment.
WHAT THIS MEANS FOR 802.11bf:
- Presence detection (amplitude variance): Group delay, SFO, CFO all cancel in relative measurements. Great.
- Breathing rate (phase at 0.2Hz): SFO drift is the main enemy. Correctable with good preprocessing. Workable.
- Gesture recognition (Doppler shifts at 1-10Hz): CFO residual starts to matter. Need careful calibration or per-packet conjugate multiplication.
- AoA / ToF sensing within 802.11bf: Group delay is fatal for absolute measurement. Per-unit factory calibration required. Most commercial systems simply don't do this and use probabilistic fingerprinting instead.
For your consultancy, this is an important boundary to set with clients: "Our 802.11bf sensing implementation will work well for X, Y, Z use cases. For centimetre-accurate AoA, we'll need factory calibration steps in your manufacturing process."
REFS:
- Keerativoranan et al. (2018) "Mitigation of CSI Temporal Phase Rotation with B2B Calibration" — Sensors MDPI
- Gjengset et al. (2011) "Phaser" — MobiCom
- Wu et al. (2012) "FILA: Fine-grained Indoor Localization" — IEEE INFOCOM (section on SFO/CFO)
- YouTube playlist: https://www.youtube.com/watch?v=TuVu4qA61Ok&list=PLXJsNZqZEF9YI_whgRZsCdER90QbKgaWx
- YouTube 11az calibration: https://www.youtube.com/watch?v=eMnPiJrPhPA

## Slide 34
BACKUP — IoT vs HOME vs ENTERPRISE
IoT vs Home vs Enterprise — Sensing Deployment Contrast
Same 802.11bf protocol — radically different constraints, different commercial paths
IoT / Industrial
Strengths
• Low-cost nodes (ESP32-C6 ~$4)
• Battery / energy-harvesting
• Edge inference on MCU
• Factory / warehouse / cold chain
Specific Challenges
• Duty cycle breaks CSI continuity
• 802.11bf MAC too heavy for small MCU
• <1 Mbps link limits CSI bandwidth
• No NPU for complex ML on constrained SoC
• Interop with legacy SCADA / OT networks
Home / Consumer
Strengths
• Full 802.11ax/be AP — mains powered
• Always-on sensing possible
• ISP service bundle opportunity
• Matter integration for smart home events
Specific Challenges
• Privacy sensitivity highest
• Zero-config requirement (consumer)
• Apartment congestion — CCA storms
• Must survive OTA firmware updates
• Mixed brand devices — normalisation
Enterprise / Campus
Strengths
• Managed APs with centralised controller
• Multi-AP fusion solved at controller
• IT team for calibration / maintenance
• Compliance and audit frameworks exist
Specific Challenges
• High-density STAs → frequent CCA defer
• Who owns sensing data — legal liability
• Legacy AP installed base, firmware lag
• Roaming (802.11r) breaks sensing sessions
• Multiple BSSIDs on same radio confound CSI
Notes: IoT vs HOME vs ENTERPRISE
The 802.11bf MAC session management (SMSR/NDP/SMR) is non-trivial to implement on a microcontroller. The ESP32-C6 has a 160MHz RISC-V core and 512KB SRAM. The 802.11bf SI role (Sensing Initiator — typically the AP) requires managing: SMSR negotiation state machine, NDP transmission scheduling, SMR parsing, coexistence with data traffic. Espressif's ESP-IDF currently exposes CSI via esp_wifi_set_csi() but without the 802.11bf session layer. Full 802.11bf MAC on ESP32-C6 is a firmware project of roughly 6-12 months of engineering. Espressif will likely ship this as an ESP-IDF component — watch their GitHub.
Battery-powered IoT sensing: The key insight is "event-triggered sensing." Don't do continuous CSI collection at 100Hz — that drains a CR2032 in hours. Instead: use a low-power motion wake-up (PIR or accelerometer), trigger 802.11bf sensing session for 5-10 seconds, make inference, go back to sleep. This is exactly what the 802.11bf sensing instance (start/stop) model supports. The SMIT (Sensing Measurement Instance Termination) frame is your power management trigger.
ENTERPRISE — THE NEAR-TERM COMMERCIAL OPPORTUNITY:
This is where Dotstar should focus first for revenue. The multi-AP fusion problem (which 802.11bf doesn't standardise for Sub-7 GHz) is PRACTICALLY SOLVED in enterprise deployments — the centralised controller (Cisco DNA, Aruba Central, Juniper Mist) knows the AP layout, can time-synchronise bistatic sensing sessions across APs, and can fuse CSI streams at the controller layer. Cisco Spaces already offers occupancy analytics using their proprietary AP sensing. 802.11bf gives this a standard foundation. 802.11bf on Cisco/Aruba/Arista APs = massive addressable market.
Roaming (802.11r/k/v) breaking sensing sessions is a real issue: when a STA roams, the sensing session context is lost. 802.11bf doesn't define session continuity across roaming. Enterprise deployments handle this by anchor-AP-based sensing (the AP closest to the sensing target maintains the session).
HOME — THE VOLUME MARKET (2027+):
ISP play: AT&T, Comcast, SoftBank, Deutsche Telekom are all watching this. The router sits in the home always-on, it has power, it has Wi-Fi — adding Wi-Fi sensing is zero additional hardware. The WFA "AP-based home monitoring" use case is literally this. But consumer privacy regulations (GDPR in EU, various state laws in US) will gate deployment in key markets.
REFS:
- Espressif ESP-IDF CSI: https://docs.espressif.com/projects/esp-idf/en/latest/esp32c6/api-guides/wifi.html
- Cisco Spaces: https://spaces.cisco.com/
- HPE Aruba occupancy sensing whitepaper: HPE.com 2024

## Slide 35
BACKUP — 802.11bf vs 802.11az
802.11bf vs 802.11az — Sensing, Ranging & Coexistence
Two standards, shared NDP foundation — different goals, architecturally complementary
802.11az — Next Generation Positioning
Goal
Sub-metre indoor positioning / FTM ranging
Mechanism
HE Ranging NDP + RTT (Round Trip Time)
Primary output
ToF / distance — not raw CSI
Architecture
STA initiates, AP responds (FTM initiator)
Phase data
Available, used for AoA refinement
Status
Ratified 2022. FTM widely deployed in phones.
Use cases
Indoor navigation, asset tracking, keyless entry
802.11bf — WLAN Sensing
Goal
Characterise environment / detect scene changes
Mechanism
NDP + full CSI matrix in SMR
Primary output
H[Nrx x Ntx x Nsc] — full CSI matrix
Architecture
SI/SR roles; unassociated sensing in Phase 2
Phase data
Critical — variance/Doppler encode scene info
Status
Ratified Sep 2025 (802.11bf-2025)
Use cases
Presence, gesture, vitals, activity, fall detection
Shared foundation: Both use HE Ranging NDP frames from 802.11ax. WFA 802.11bf AP cert Req 2 is literally the same heNDP capability as 802.11az ranging. Architecturally aligned at PHY; diverge at MAC (what you do with the measurements). A device can simultaneously participate in FTM (ranging) and CSI sensing (802.11bf) sessions.
Notes: 11bf vs 11az — ANSWER TO THE INEVITABLE Q&A QUESTION
This question always comes up from Wi-Fi positioning engineers. Clean answer:
802.11az (NGP, ratified 2022) = RANGING. Goal is "how far away is this device?" Output is RTT → distance. FTM (Fine Timing Measurement) is widely deployed already — Pixel 6+, Galaxy S20+, Nest Hub all support FTM. Practical accuracy: 1-3 metres typical, sub-metre in good conditions with 802.11az enhanced mode.
802.11bf (2025) = ENVIRONMENT SENSING. Goal is "what is happening around my devices?" Output is the full CSI H matrix. You're characterising the channel, not measuring distance to a device.
WHY THE SHARED NDP?
Null Data Packets are the cleanest channel probe in 802.11 — no payload to confound the channel estimate. Both 802.11az and 802.11bf inherit the HE Ranging NDP from 802.11ax. This is why WFA 802.11bf AP cert Req 2 "transmit/receive HE Ranging NDP" is essentially the same capability test as 802.11az ranging compliance. A chip that passes one is mostly ready for the other.
THE GROUP DELAY CONNECTION:
The "ranging never works" argument from the YouTube talk is specifically about 802.11az FTM accuracy. Group delay in the RF front-end creates a per-chip, per-frequency timing offset that cannot be calibrated over the air. For 802.11az ranging, this limits accuracy to ~30cm even in ideal conditions on COTS silicon. For 802.11bf sensing, if you're doing RELATIVE measurements (motion detection, breathing rate) the group delay is a static offset that cancels. But if you try to do absolute ToF-based ranging within 802.11bf (which the standard supports), you hit the same wall.
COEXISTENCE IN PRACTICE:
A Wi-Fi 6E AP that supports both 802.11az and 802.11bf can run both simultaneously. FTM sessions for positioning run at low frequency (1-2Hz bursts). CSI sensing sessions run at higher frequency (10-100Hz continuous). Both use EDCA, both defer to CCA. The 802.11bf SI can schedule sensing periods to avoid FTM exchange windows if needed. In practice there's minimal conflict — the traffic volumes are very different.
REFS:
- IEEE 802.11az-2022: https://standards.ieee.org/ieee/802.11az/
- IEEE 802.11bf-2025: https://standards.ieee.org/ieee/802.11bf/11574/
- YouTube Wi-Fi Ranging: https://www.youtube.com/watch?v=TuVu4qA61Ok
- YouTube 802.11az calibration: https://www.youtube.com/watch?v=eMnPiJrPhPA

## Slide 36
BACKUP — MAC/PHY REFERENCE
802.11bf MAC/PHY Technical Reference — Engineer Q&A
Four technical questions Wi-Fi engineers will ask — the answers
Sensing NDP Frame Structure
HE Ranging NDP uses 2x HE-LTF symbol duration (mandatory ). Each spatial stream gets one or more LTF symbols — multiple LTF repetitions per stream are supported . SR derives channel estimate from LTF correlation; the resulting CSI is then grouped by Ng before reporting. Ng=4 mandatory : floor(242/4) = 60 groups per stream at 20 MHz. NOT 234 raw subcarrier values — the LTF processing + Ng grouping is the actual output chain.
SMR Format & Data Volume
SMR CSI encoding per spec §9.4: Each Tx-Rx pair has a 12-bit scaling factor. Per subcarrier group: 8-bit real (I) + 8-bit imaginary (Q) = 16 bits = 2 bytes per group per stream. At Ng=4, 20 MHz (60 groups), 2×2 MIMO (4 Tx-Rx pairs): 4×[12-bit scale] + 60×4×2 bytes = 486 bytes/SMR ≈ 0.5 KB. At 100 Hz: ~48 KB/s data + headers. Padding: if odd number of scaling factors, 4-bit pad added. Note: CSI is HE-LTF-derived and Ng-grouped — NOT raw ADC subcarrier values.
PASN — Pre-Association Security
PASN (from 802.11be) enables secure frame exchange WITHOUT full association — critical for Phase 2 unassociated sensing. Uses Diffie-Hellman (P-256/P-384) + AES-GCM to establish session key between SI and SR. Sensing NDPs and SMRs are then MAC-layer encrypted. WFA AP cert Req 1 = PASN transmit+receive. Implementation: relatively heavyweight for IoT MCUs (~8KB RAM for ECDH). Full hostap support available since 2022.
Coexistence & CCA Impact
Sensing sessions default to EDCA AC_BE. SMSR can request AC_VI for latency-sensitive sensing. NDP exchange uses SIFS-based back-to-back framing within a TXOP. CCA deferral breaks sensing continuity — 802.11bf defines max_sensing_gap field in SMR header that allows SR to flag unreliable data if gap > threshold. At 70% channel utilisation (typical enterprise), sensing continuity drops to ~85%. Planning: use sensing sessions during off-peak hours or dedicate a secondary radio.
Notes: MAC/PHY DEEP DIVE — for the hardware/firmware engineers in Q&A
SENSING NDP:
The key difference between a regular HE NDP (used for MU-MIMO beamforming feedback) and a sensing NDP is the number of HE-LTF symbols. For beamforming, you need Nsts x NLTF for a 1-stream estimate. For sensing, you want HIGHER SNR on the channel estimate, so 802.11bf recommends using more LTF symbols (increased sensing measurement time, or "NSMT" in the standard). More LTF = more SNR = better CSI quality. Trade-off: more airtime consumed per sensing cycle. This is configurable in the SMSR.
SMR DATA VOLUME:
The numbers above are important for system design. At 100Hz with 2x2 MIMO and Ng=4 in 20MHz: 92.8KB/s from SR to SI. If you're doing sensing in a Wi-Fi network with 802.11be (Wi-Fi 7) that has 4x4 MIMO and 80MHz bandwidth at Ng=1, that's: 8 streams x 996 subcarriers x 4 bytes = 31.9KB per frame x 100Hz = 3.2MB/s. This rivals a video stream. Compressed SMR or reduced sampling rate is mandatory at scale.
PASN IMPLEMENTATION NOTE:
If your client is building an 802.11bf SI (typically an AP), PASN is already in hostap 2.10+ (2022). If building an SR on embedded Linux or FreeRTOS, you'll need to port the ECDH key exchange. On Cortex-M33 (e.g., Nordic nRF9160 or STM32WL55), this takes ~200ms per handshake — acceptable for session setup (happens once per sensing period). On ESP32-C6's RISC-V, mbedTLS handles this cleanly.
CCA PLANNING:
For a production 802.11bf sensing deployment, you should model sensing availability as a function of channel utilisation. Rule of thumb: at U% channel utilisation, sensing availability ≈ (100-U)% of planned sensing cycles, assuming random backoff. At U=30% (typical home), availability ≈ 70% — fine. At U=70% (enterprise open office), availability ≈ 30% — may need sensing priority upgrade to AC_VI or a dedicated sensing BSSID.
REFS:
- IEEE 802.11bf-2025, Section 9.4 (SMR frame format), Section 11 (sensing procedures)
- IEEE 802.11az-2022, Section 9.3.4 (HE Ranging NDP LTF structure)
- PASN: IEEE 802.11be-2024, Section 12.7.7 and hostap implementation
- 802.11 EDCA: IEEE 802.11-2024, Section 10.22

## Slide 37
BACKUP — STFT SPECTROGRAM
CSI Doppler Spectrogram — Reading a Fall Detection Signature
Same 802.11bf CSI stream · X-axis = time · Y-axis = velocity (Doppler frequency) · Color = signal energy
High
freq
Low
freq
◀ no motion
peak energy ▶
① Pre-fall
Breathing (0–1.9s)
Faint band at bottom only — chest rising/falling at ~0.3 Hz (breathing rhythm). Everything above = dark = no fast movement.
② Fall onset
Body tipping (1.9–2.9s)
Energy climbs upward into mid/high frequencies — muscles firing, arms flailing. Velocity increasing second by second.
③ Impact peak
Floor contact (2.9–3.5s)
Entire column blazes red simultaneously — body hits floor, every part stops at once. Broadband burst across all freq = diagnostic signature.
④ Post-fall
Stillness (3.5–5s)
Abrupt near-total darkness. Person lying still, velocity = 0 Hz. Bright burst → immediate black = the classifier trigger.
Notes: BACKUP — STFT SPECTROGRAM READING GUIDE
HOW TO READ THIS SLIDE:
X-axis = time (left=0s, right=5s). Y-axis = Doppler frequency = velocity. Bottom = slow (breathing). Top = fast (impact). Color = energy: dark=silence, cyan=moderate, red=peak.
PHASE 1 (blue, 0-1.9s): Pre-fall. Only faint band at very bottom = chest breathing at 0.3 Hz. Above that = dark = person standing still, no fast motion.
PHASE 2 (amber, 1.9-2.9s): Fall onset. Energy climbs upward as body tips. Muscles firing, arms flailing, velocity increasing.
PHASE 3 (red, 2.9-3.5s): Impact. Entire column lights up simultaneously = body hitting floor, every part stops at once = broadband burst = diagnostic signature.
PHASE 4 (grey, 3.5-5s): Stillness. Abrupt darkness = person lying still = velocity 0 Hz.
KEY: The pattern bright-burst then immediate-darkness is what the classifier detects. An FFT would average all time into one spectrum and lose the sequence entirely. STFT preserves the timeline.